## Slide 1: Chapter 3 Transport Layer
Computer Networking: A Top Down Approach
6th edition
Jim Kurose, Keith Ross Addison-Wesley March 2012
A note on the use of these ppt slides:
We’re making these slides freely available to all (faculty, students, readers). They’re in PowerPoint form so you see the animations; and can add, modify, and delete slides (including this one) and slide content to suit your needs.
They obviously represent a lot of work on our part. In return for use, we only ask the following:
If you use these slides (e.g., in a class) that you mention their source
(after all, we’d like people to use our book!)
If you post any slides on a www site, that you note that they are adapted from (or perhaps identical to) our slides, and note our copyright of this material.
Thanks and enjoy! JFK/KWR
All material copyright 1996-2013
J.F Kurose and K.W. Ross, All Rights Reserved

## Slide 2: Chapter 3: Transport Layer
our goals:
understand principles behind transport layer services:
  multiplexing, demultiplexing
  reliable data transfer
  flow control
  congestion control
learn about Internet transport layer protocols:
  UDP: connectionless transport
  TCP: connection-oriented reliable transport
  TCP congestion control

## Slide 3: Chapter 3 outline
  transport-layer services
  multiplexing and demultiplexing
  connectionless transport: UDP
  principles of reliable data transfer
  connection-oriented transport: TCP
    segment structure
    reliable data transfer
    flow control
    connection management
  principles of congestion control
  TCP congestion control

## Slide 4: Transport services and protocols

provide logical communication between app processes running on different hosts
transport protocols run in end systems
send side: breaks app messages into segments, passes to network layer
rcv side: reassembles segments into messages, passes to app layer
more than one transport protocol available to apps
Internet: TCP and UDP


application
transport
network
data link
physical
logical end-end transport
application transport
network
data link
physical

## Slide 5: Transport vs. network layer
 network layer: logical
communication between hosts

transport layer:
logical
communication between processes
 relies on, enhances,
network layer services





household analogy:
12 kids in Ann’s house sending
letters to 12 kids in Bill’s house:
hosts = houses processes = kids
app messages = letters in envelopes
transport protocol = Ann
and Bill who demux to in- house siblings
network-layer protocol = postal service

## Slide 6: Internet transport-layer protocols
reliable, in-order delivery (TCP)
  congestion control
  flow control
  connection setup
unreliable, unordered delivery: UDP
  no-frills extension of “best-effort” IP
services not available:
  delay guarantees
  bandwidth guarantees
application
transport network
data link physical
application
transport network
data link physical
network
data link
physical
network data link physical
network data link physical
network
data link physical
network
data link
network physical
data link
physical
network
data link
physical
logical end-end transport

## Slide 7: Chapter 3 outline
  transport-layer services
  multiplexing and demultiplexing
  connectionless transport: UDP
  principles of reliable data transfer
  connection-oriented transport: TCP
    segment structure
    reliable data transfer
    flow control
    connection management
  principles of congestion control
  TCP congestion control

## Slide 8: Multiplexing/demultiplexing
socket
process
use header info to deliver
received segments to correct socket
demultiplexing at receiver:
handle data from multiple
sockets, add transport header (later used for demultiplexing)
multiplexing at sender:
transport
physical
link
network
application
P1 P2
transport
physical
link
network
application
P4
transport
physical
link
network
application
P3

## Slide 9: How demultiplexing works
source port # | dest port #
other header fields | 
application data (payload) | 
host receives IP datagrams
  each datagram has source IP address, destination IP address
  each datagram carries one transport-layer segment
  each segment has source, destination port number
host uses IP addresses & port numbers to direct segment to appropriate socket
32 bits
TCP/UDP segment format

## Slide 10: Connectionless demultiplexing
recall: created socket has host-local port #:
DatagramSocket mySocket1
= new DatagramSocket(12534);
  when host receives UDP segment:
    checks destination port # in segment
    directs UDP segment to socket with that port #
recall: when creating datagram to send into UDP socket, must specify
  destination IP address
  destination port #
IP datagrams with same dest. port #, but different source IP addresses and/or source port numbers will be directed to same socket at dest

## Slide 11: Connectionless demux: example
DatagramSocket serverSocket = new
DatagramSocket (6428);
link physical
network
application
P3
transport
transport
physical
l
ink
network
application
P1
transpo
rt
physical
link
netwo
rk
application
P4
DatagramSocket mySocket1 = new
DatagramSocket
(5775);
DatagramSocket
mySocket2 = new DatagramSocket
(9157);
source port: 9157
dest port: 6428
source port: 6428
dest port: 9157
source port: ?
dest port: ?
source port: ? dest port: ?

## Slide 12: Connection-oriented demux
TCP socket identified by 4-tuple:
  source IP address
  source port number
  dest IP address
  dest port number
demux: receiver uses all four values to direct segment to appropriate socket
server host may support many simultaneous TCP sockets:
  each socket identified by its own 4-tuple
web servers have different sockets for each connecting client
  non-persistent HTTP will have different socket for each request

## Slide 13: Connection-oriented demux: example
Transport Layer 3-13
transport
physical
link
network
application
P3
transport
physical
link
network
source IP,port: A,9157 dest IP, port: B,80
source IP,port: B,80 dest IP,port: A,9157
host: IP address A
host: IP address C
transport network link physical
application
P4 P5 P6
application
P2 P3
source IP,port: C,5775 dest IP,port: B,80
source IP,port: C,9157 dest IP,port: B,80
three segments, all destined to IP address: B, dest port: 80 are demultiplexed to different sockets
server: IP address B

## Slide 14: Connection-oriented demux: example
transport
physical
link
network
application
P3
transport
physical
link
network
source IP,port: A,9157 dest IP, port: B,80
source IP,port: B,80 dest IP,port: A,9157
host: IP address A
host: IP address C
server: IP address B
transport network link physical
application
P2 P3
source IP,port: C,5775 dest IP,port: B,80
source IP,port: C,9157 dest IP,port: B,80
application
P4
threaded server

## Slide 15: Chapter 3 outline
  transport-layer services
  multiplexing and demultiplexing
  connectionless transport: UDP
  principles of reliable data transfer
  connection-oriented transport: TCP
    segment structure
    reliable data transfer
    flow control
    connection management
  principles of congestion control
  TCP congestion control

## Slide 16: UDP: User Datagram Protocol [RFC 768]

“no frills,” “bare bones” Internet transport protocol
“best effort” service, UDP segments may be:
lost
delivered out-of-order to app
connectionless:
no handshaking between UDP sender, receiver
each UDP segment handled independently of others


UDP use:
  streaming multimedia apps (loss tolerant, rate sensitive)
  DNS
  SNMP
reliable transfer over UDP:
  add reliability at application layer
  application-specific error recovery!

## Slide 17: UDP: segment header
32 bits
UDP segment format
source port # | dest port #
length | checksum
application data (payload) | 
length, in bytes of UDP segment, including header




no connection establishment (which can add delay)
simple: no connection state at sender, receiver
small header size
no congestion control: UDP can blast away as fast as desired
why is there a UDP?

## Slide 18: UDP segment Header (Cont..)
The port numbers allow the destination host to pass the application data to the correct process running on the destination end system
The length field specifies the number of bytes in the UDP segment (header plus data).
The checksum is used by the receiving host to check whether errors have been introduced into the segment.

## Slide 19: UDP checksum
sender:

treat segment contents, including header fields, as sequence of 16-bit integers
checksum: addition (one’s complement sum) of segment contents
sender puts checksum value into UDP checksum field


receiver:

compute checksum of received segment
check if computed checksum equals checksum field value:
NO - error detected
YES - no error detected.
But maybe errors nonetheless? More later
….

Goal: detect “errors” (e.g., flipped bits) in transmitted segment

## Slide 20: Internet checksum: example
example: add two 16-bit integers
1 1 1 0 0 1 1 0 0 1 1 0 0 1 1 0
1 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1
1 1 0 1 1 1 0 1 1 1 0 1 1 1 0 1 1
1 0 1 1 1 0 1 1 1 0 1 1 1 1 0 0
0 1 0 0 0 1 0 0 0 1 0 0 0 0 1 1
wraparound
sum checksum
Note: when adding numbers, a carryout from the most significant bit needs to be added to the result

## Slide 21: Chapter 3 outline
  transport-layer services
  multiplexing and demultiplexing
  connectionless transport: UDP
  principles of reliable data transfer
  connection-oriented transport: TCP
    segment structure
    reliable data transfer
    flow control
    connection management
  principles of congestion control
  TCP congestion control

## Slide 22: Principles of reliable data transfer
 important in application, transport, link layers
 top-10 list of important networking topics!
characteristics of unreliable channel will determine complexity of reliable data transfer protocol (rdt)


## Slide 23: Principles of reliable data transfer
characteristics of unreliable channel will determine complexity of reliable data transfer protocol (rdt)

 important in application, transport, link layers
 top-10 list of important networking topics!

## Slide 24: Principles of reliable data transfer
 important in application, transport, link layers
 top-10 list of important networking topics!
characteristics of unreliable channel will determine complexity of reliable data transfer protocol (rdt)


## Slide 25: Reliable data transfer: getting started
send side
receive side
rdt_send(): called from above, (e.g., by app.). Passed data to deliver to receiver upper layer
udt_send(): called by rdt, to transfer packet over unreliable channel to receiver
rdt_rcv(): called when packet arrives on rcv-side of channel
deliver_data(): called by rdt to deliver data to upper

## Slide 26: Reliable data transfer: getting started
we’ll:
incrementally develop sender, receiver sides of reliable data transfer protocol (rdt)
consider only unidirectional data transfer
 but control info will flow on both directions!
use finite state machines (FSM) to specify sender, receiver
event causing state transition
actions taken on state transition
state 1
state 2
state: when in this “state” next state uniquely determined by next
event
event actions

## Slide 27: rdt1.0: reliable transfer over a reliable channel
underlying channel perfectly reliable
  no bit errors
  no loss of packets
separate FSMs for sender, receiver:
  sender sends data into underlying channel
  receiver reads data from underlying channel
Wait for call from above
packet = make_pkt(data) udt_send(packet)
rdt_send(data)
extract (packet,data) deliver_data(data)
Wait for call from below
rdt_rcv(packet)
sender
receiver

## Slide 28: rdt2.0: channel with bit errors
underlying channel may flip bits in packet
 checksum to detect bit errors
the question: how to recover from errors:
 acknowledgements (ACKs): receiver explicitly tells sender that pkt received OK
 negative acknowledgements (NAKs): receiver explicitly tells sender that pkt had errors
 sender retransmits pkt on receipt of NAK
 new mechanisms in rdt2.0 (beyond rdt1.0):
 error detection
 receiver feedback: control msgs (ACK,NAK) rcvr-
>sender
How do humans recover from “errors” during conversation?

## Slide 29: rdt2.0: channel with bit errors
underlying channel may flip bits in packet
  checksum to detect bit errors
the question: how to recover from errors:
  acknowledgements (ACKs): receiver explicitly tells sender that pkt received OK
  negative acknowledgements (NAKs): receiver explicitly tells sender that pkt had errors
  sender retransmits pkt on receipt of NAK
new mechanisms in rdt2.0 (beyond rdt1.0):
  error detection
  feedback: control msgs (ACK,NAK) from receiver to sender

## Slide 30: rdt2.0: FSM specification
Wait for call from above
rdt_rcv(rcvpkt) && notcorrupt(rcvpkt)
extract(rcvpkt,data) deliver_data(data) udt_send(ACK)
sndpkt = make_pkt(data, checksum) udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
rdt_rcv(rcvpkt) && isACK(rcvpkt)
udt_send(sndpkt)
isNAK(rcvpkt)
udt_send(NAK)
rdt_rcv(rcvpkt) && corrupt(rcvpkt)
Wait for ACK or NAK
Wait for call from below

sender
receiver
rdt_send(data)

## Slide 31: rdt2.0: operation with no errors
Wait for call from above
rdt_rcv(rcvpkt) && notcorrupt(rcvpkt)
extract(rcvpkt,data) deliver_data(data) udt_send(ACK)
rdt_rcv(rcvpkt) && isACK(rcvpkt)
udt_send(sndpkt)
isNAK(rcvpkt)
udt_send(NAK)
rdt_rcv(rcvpkt) && corrupt(rcvpkt)
Wait for ACK or NAK
Wait for call from below
rdt_send(data)
snkpkt = make_pkt(data, checksum) udt_send(sndpkt)
rdt_rcv(rcvpkt) &&


## Slide 32: rdt2.0: error scenario
Wait for call from above
rdt_rcv(rcvpkt) && notcorrupt(rcvpkt)
extract(rcvpkt,data) deliver_data(data) udt_send(ACK)
rdt_rcv(rcvpkt) && isACK(rcvpkt)
udt_send(sndpkt)
rdt_rcv(rcvpkt) && isNAK(rcvpkt)
udt_send(NAK)
rdt_rcv(rcvpkt) && corrupt(rcvpkt)
Wait for ACK or NAK
Wait for call from below
rdt_send(data)
snkpkt = make_pkt(data, checksum) udt_send(sndpkt)


## Slide 33: rdt2.0 has a fatal flaw!
what happens if ACK/NAK corrupted?

sender doesn’t know what happened at receiver!
can’t just retransmit: possible duplicate

handling duplicates:

sender retransmits current pkt if ACK/NAK corrupted
sender adds sequence number to each pkt
receiver discards (doesn’t deliver up) duplicate pkt


stop and wait
sender sends one packet, then waits for receiver response

## Slide 34: rdt2.1: sender, handles garbled ACK/NAKs
Wait for call 0 from above
udt_send(sndpkt)
rdt_send(data)
sndpkt = make_pkt(0, data, checksum)
Wait for ACK or NAK 0
rdt_rcv(rcvpkt) && ( corrupt(rcvpkt) || isNAK(rcvpkt) ) udt_send(sndpkt)
sndpkt = make_pkt(1, data, checksum) udt_send(sndpkt)
rdt_send(data)
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt) && isACK(rcvpkt)
udt_send(sndpkt)
rdt_rcv(rcvpkt) && ( corrupt(rcvpkt) || isNAK(rcvpkt) )
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt) && isACK(rcvpkt)
Wait for call 1 from above
Wait for ACK or NAK 1



## Slide 35: rdt2.1: receiver, handles garbled ACK/NAKs
Wait for 0 from below
sndpkt = make_pkt(NAK, chksum) udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
not corrupt(rcvpkt) && has_seq0(rcvpkt)
rdt_rcv(rcvpkt) && notcorrupt(rcvpkt) && has_seq1(rcvpkt)
extract(rcvpkt,data) deliver_data(data)
sndpkt = make_pkt(ACK, chksum) udt_send(sndpkt)
Wait for 1 from below
rdt_rcv(rcvpkt) && notcorrupt(rcvpkt) && has_seq0(rcvpkt)
extract(rcvpkt,data) deliver_data(data)
sndpkt = make_pkt(ACK, chksum) udt_send(sndpkt)
rdt_rcv(rcvpkt) && (corrupt(rcvpkt)
sndpkt = make_pkt(ACK, chksum) udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
not corrupt(rcvpkt) && has_seq1(rcvpkt)
rdt_rcv(rcvpkt) && (corrupt(rcvpkt)
sndpkt = make_pkt(ACK, chksum) udt_send(sndpkt)
sndpkt = make_pkt(NAK, chksum) udt_send(sndpkt)

## Slide 36: rdt2.1: discussion
sender:
seq # added to pkt
two seq. #’s (0,1) will suffice. Why?
must check if received ACK/NAK corrupted
twice as many states
 state must “remember” whether “expected” pkt should have seq # of 0 or 1
receiver:
must check if received packet is duplicate
 state indicates whether 0 or 1 is expected pkt seq #
note: receiver can not know if its last ACK/NAK received OK at sender

## Slide 37: rdt2.2: a NAK-free protocol
same functionality as rdt2.1, using ACKs only
instead of NAK, receiver sends ACK for last pkt received OK
 receiver must explicitly include seq # of pkt being ACKed
duplicate ACK at sender results in same action as NAK: retransmit current pkt

## Slide 38: rdt2.2: sender, receiver fragments
Transport Layer 3-37
Wait for call 0 from above
udt_send(sndpkt)
rdt_send(data)
sndpkt = make_pkt(0, data, checksum)
rdt_rcv(rcvpkt) && ( corrupt(rcvpkt) || isACK(rcvpkt,1) )
udt_send(sndpkt)
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt) && isACK(rcvpkt,0)
Wait for ACK
0
sender FSM fragment
rdt_rcv(rcvpkt) && notcorrupt(rcvpkt) && has_seq1(rcvpkt)
extract(rcvpkt,data) deliver_data(data)
sndpkt = make_pkt(ACK1, chksum)
udt_send(sndpkt)
Wait for 0 from below
rdt_rcv(rcvpkt) && (corrupt(rcvpkt) || has_seq1(rcvpkt))
udt_send(sndpkt)
receiver FSM fragment


## Slide 39: rdt3.0: channels with errors and loss
new assumption: underlying channel can also lose packets (data, ACKs)
 checksum, seq. #, ACKs, retransmissions will be of help … but not enough



approach: sender waits “reasonable” amount of time for ACK
retransmits if no ACK received in this time
if pkt (or ACK) just delayed (not lost):
retransmission will be duplicate, but seq. #’s already handles this
receiver must specify seq # of pkt being ACKed
requires countdown timer

## Slide 40: rdt3.0 sender
sndpkt = make_pkt(0, data, checksum) udt_send(sndpkt)
start_timer
rdt_send(data)
Wait for ACK0
Wait for call 1 from above
sndpkt = make_pkt(1, data, checksum) udt_send(sndpkt)
start_timer
rdt_send(data)
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt) && isACK(rcvpkt,0)
rdt_rcv(rcvpkt) &&
( corrupt(rcvpkt) || isACK(rcvpkt,0) )
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt) && isACK(rcvpkt,1)
stop_timer
stop_timer
timeout udt_send(sndpkt) start_timer
rdt_rcv(rcvpkt)
Wait for call 0from above
Wait for ACK1
rdt_rcv(rcvpkt)

rdt_rcv(rcvpkt) && ( corrupt(rcvpkt) || isACK(rcvpkt,1) )

timeout udt_send(sndpkt) start_timer


## Slide 41: rdt3.0 in action
rcv pkt1 send ack1
rcv pkt0
send ack0
sender receiver
send pkt0
send ack0
rcv ack0 send pkt1
rcv ack1 send pkt0
rcv pkt0
pkt0
ack1
pkt0
ack0 pkt1
ack0
(a) no loss
sender
send pkt0
receiver
rcv pkt1
rcv pkt0
send ack0
send ack1
send ack0
rcv ack0 send pkt1
rcv ack1 send pkt0
rcv pkt0
pkt0
ack0
ack1
pkt0
ack0
(b) packet loss
pkt1
X
loss
pkt1
timeout
resend pkt1

## Slide 42: rdt3.0 in action
rcv pkt1 send ack1
(detect duplicate)
rcv pkt1
rcv pkt0
send ack0
send ack1
send ack0
rcv ack0 send pkt1
sender receiver
send pkt0
rcv ack1 send pkt0
rcv pkt0
pkt0
ack1
pkt0
ack0 pkt1
ack0
(c) ACK loss
ack1
X
loss
pkt1
timeout
resend pkt1
rcv pkt1 send ack1
(detect duplicate)
sender
send pkt0
receiver
rcv pkt1
send ack0
rcv ack0 send pkt1
rcv pkt0
pkt0
ack0 pkt1
(d) premature timeout/ delayed ACK
timeout
resend pkt1
ack1
send ack1
send pkt0
rcv ack1 send pkt0
rcv ack1
pkt1
pkt0 ack1
ack0
pkt0
ack0
rcv pkt0
send ack0 rcv pkt0
send ack0
(detect duplicate)

## Slide 43: Performance of rdt3.0
rdt3.0 is correct, but performance stinks
e.g.: 1 Gbps link, 15 ms prop. delay, 8000 bit packet:
 U sender: utilization – fraction of time sender busy sending
U
sender
30.008
L / R .008
0.00027
RTT + L / R
= = =
 if RTT=30 msec, 1KB pkt every 30 msec: 33kB/sec thruput over 1 Gbps link
 network protocol limits use of physical resources!
Dtrans =
L
R
8000 bits
109 bits/sec
=
= 8 microsecs

## Slide 44: rdt3.0: stop-and-wait operation
sender
receiver
RTT
first packet bit transmitted, t = 0 last packet bit transmitted, t = L / R
first packet bit arrives
last packet bit arrives, send ACK
ACK arrives, send next packet, t = RTT + L / R
U
sender
=
.008
30.008
=
0.00027
L / R
RTT + L / R
=

## Slide 45: Pipelined protocols
pipelining: sender allows multiple, “in-flight”, yet- to-be-acknowledged pkts
range of sequence numbers must be increased
buffering at sender and/or receiver
 two generic forms of pipelined protocols: go-Back-N, selective repeat

## Slide 46: Pipelining: increased utilization
first packet bit transmitted, t = 0 last bit transmitted, t = L / R
sender receiver
RTT
ACK arrives, send next packet, t = RTT + L / R
first packet bit arrives
last packet bit arrives, send ACK
last bit of 2nd packet arrives, send ACK last bit of 3rd packet arrives, send ACK
3-packet pipelining increases utilization by a factor of 3!
U
sender
=
.0024
30.008
= 0.00081
3L / R
RTT + L / R
=

## Slide 47: Pipelined protocols: overview
Go-back-N:
sender can have up to N unacked packets in pipeline
receiver only sends
cumulative ack
  doesn’t ack packet if there’s a gap
sender has timer for oldest unacked packet
  when timer expires, retransmit all unacked packets
Selective Repeat:
sender can have up to N unack’ed packets in pipeline
rcvr sends individual ack
for each packet
sender maintains timer for each unacked packet
 when timer expires, retransmit only that unacked packet

## Slide 48: Go-Back-N: sender


k-bit seq # in pkt header
“window” of up to N, consecutive unack’ed pkts allowed

ACK(n): ACKs all pkts up to, including seq # n - “cumulative ACK”
 may receive duplicate ACKs (see receiver) timer for oldest in-flight pkt
timeout(n): retransmit packet n and all higher seq # pkts in window



## Slide 49: GBN: sender extended FSM
Transport Layer 3-48
Wait
1])
timeout start_timer udt_send(sndpkt[base]) udt_send(sndpkt[base+1])
… udt_send(sndpkt[nextseqnum-
rdt_send(data)
if (nextseqnum < base+N) {
sndpkt[nextseqnum] = make_pkt(nextseqnum,data,chksum) udt_send(sndpkt[nextseqnum])
if (base == nextseqnum) start_timer
nextseqnum++
}
else
refuse_data(data)
base = getacknum(rcvpkt)+1 If (base == nextseqnum)
stop_timer else
start_timer
rdt_rcv(rcvpkt) &&
notcorrupt(rcvpkt)
base=1 nextseqnum=1
rdt_rcv(rcvpkt)
&& corrupt(rcvpkt)


## Slide 50: GBN: receiver extended FSM
ACK-only: always send ACK for correctly-received pkt with highest in-order seq #
may generate duplicate ACKs
need only remember expectedseqnum
out-of-order pkt:
  discard (don’t buffer): no receiver buffering!
  re-ACK pkt with highest in-order seq #
Wait
udt_send(sndpkt)
default
rdt_rcv(rcvpkt)
&& notcurrupt(rcvpkt)
&& hasseqnum(rcvpkt,expectedseqnum)
extract(rcvpkt,data) deliver_data(data)
sndpkt = make_pkt(expectedseqnum,ACK,chksum) udt_send(sndpkt)
expectedseqnum++
make_pkt(expectedseqnum,ACK,chksum)

expectedseqnum=1 sndpkt =

## Slide 51: GBN in action
sender
send pkt0 send pkt1 send pkt2 send pkt3
(wait)
receiver
Xloss
receive pkt0, send ack0 receive pkt1, send ack1
receive pkt3, discard,
(re)send ack1
receive pkt4, discard,
(re)send ack1 receive pkt5, discard,
(re)send ack1
ignore duplicate ACK
pkt 2 timeout send pkt2 send pkt3 send pkt4 send pkt5
rcv pkt2, deliver, send ack2 rcv pkt3, deliver, send ack3 rcv pkt4, deliver, send ack4 rcv pkt5, deliver, send ack5
sender window (N=4)
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0
1 2 3 4
5 6 7 8 rcv ack0, send pkt4
0 1
2 3 4 5
6 7 8 rcv ack1, send pkt5
0 1
0 1
0 1
0 1
6 7 8
6 7 8
6 7 8
2 3 4 5
2 3 4 5
2 3 4 5
2 3 4 5
6 7 8

## Slide 52: Selective repeat
receiver individually acknowledges all correctly received pkts
  buffers pkts, as needed, for eventual in-order delivery to upper layer
sender only resends pkts for which ACK not received
  sender timer for each unACKed pkt
sender window
  N consecutive seq #’s
  limits seq #s of sent, unACKed pkts

## Slide 53: Selective repeat: sender, receiver windows

## Slide 54: Selective repeat

if next available seq # in window, send pkt
timeout(n):

resend pkt n, restart timer
ACK(n) in [sendbase,sendbase+N]:


mark pkt n as received if n smallest unACKed
pkt, advance window base to next unACKed seq #
sender
data from above:





receiver
pkt n in [rcvbase, rcvbase+N-1]
send ACK(n)
out-of-order: buffer in-order: deliver (also
deliver buffered, in-order
pkts), advance window to next not-yet-received pkt
pkt n in [rcvbase-N,rcvbase-1]
ACK(n)
otherwise:
ignore

## Slide 55: Selective repeat in action
sender
send pkt0 send pkt1 send pkt2 send pkt3
(wait)
receiver
Xloss
receive pkt0, send ack0 receive pkt1, send ack1
receive pkt3, buffer,
send ack3
receive pkt4, buffer,
send ack4 receive pkt5, buffer,
send ack5
rcv pkt2; deliver pkt2,
pkt3, pkt4, pkt5; send ack2
sender window (N=4)
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0
1 2 3 4
5 6 7 8 rcv ack0, send pkt4
0 1
2 3 4 5
6 7 8 rcv ack1, send pkt5
0 1 | 2 3 4 5 | 6 7 8
0 1 | 2 3 4 5 | 6 7 8
0 1 | 2 3 4 5 | 6 7 8
0 1 | 2 3 4 5 | 6 7 8
record ack3 arrived
pkt 2 timeout
send pkt2
record ack4 arrived record ack5 arrived
Q: what happens when ack2 arrives?

## Slide 56
Selective repeat: dilemma
example:
receiver window (after receipt)
0 1 2
3 0 1 2
0 1 2
3 0 1 2
0 1 2
3 0 1 2
pkt0
timeout
retransmit pkt0
0
1 2 3
0 1 2
0 1
2 3 0
1 2
0 1 2
3 0 1
2
pkt0 pkt1 pkt2
X X
X
0 1 2 3 0 1 2
(b) oops!
will accept packet with seq number 0
sender window (after receipt)
0 1 2 3 0 1 2
0 1 2 3 0 1 2
0 1 2 3 0 1 2
0 1 2 3 0 1 2
0 1 2 3 0 1 2
pkt0 pkt1 pkt2
pkt3 X
pkt0
0
1 2 3
0 1 2
0 1
2 3 0
1 2
0 1 2
3 0 1
2
will accept packet with seq number 0
(a) no problem
receiver can’t see sender side. receiver behavior identical in both cases!
something’s (very) wrong!



seq #’s: 0, 1, 2, 3
window size=3
receiver sees no difference in two scenarios!
duplicate data accepted as new in (b)

Q: what relationship between seq # size and window size to avoid problem in (b)?

## Slide 57: Chapter 3 outline
  transport-layer services
  multiplexing and demultiplexing
  connectionless transport: UDP
  principles of reliable data transfer
  connection-oriented transport: TCP
    segment structure
    reliable data transfer
    flow control
    connection management
  principles of congestion control
  TCP congestion control

## Slide 58: TCP: Overview
RFCs: 793,1122,1323, 2018, 2581
full duplex data:
  bi-directional data flow in same connection
  MSS: maximum segment size
connection-oriented:
  handshaking (exchange of control msgs) inits sender, receiver state before data exchange
flow controlled:
  sender will not overwhelm receiver
point-to-point:
  one sender, one receiver
reliable, in-order byte steam:
  no “message boundaries”
pipelined:
  TCP congestion and flow control set window size

## Slide 59: TCP segment structure
application data
(variable length)
32 bits
source port # dest port # sequence number
acknowledgement number
receive window
Urg data pointer
checksum
UAP RS F
head not len used
options (variable length)
URG: urgent data (generally not used)
ACK: ACK #
valid
PSH: push data now (generally not used)
RST, SYN, FIN:
connection estab (setup, teardown commands)
# bytes rcvr willing to accept
counting by bytes of data
(not segments!)
Internet checksum (as in UDP)

## Slide 60: TCP Segment Structure(Cont..)
Source and destination port numbers, which are used for multiplexing/demultiplexing data from/to upper-layer applications.
The 32-bit sequence number field and the 32-bit acknowledgment number field are used by the TCP sender and receiver in implementing a reliable data transfer service
The sequence number for a segment is therefore the byte-stream number of the first byte in the segment
The acknowledgment number that Host A puts in its segment is the sequence number of the next byte Host A is expecting from Host B.
The 16-bit receive window field is used for flow control. It is used to indicate the number of bytes that a receiver is willing to accept.
The 4-bit header length field specifies the length of the TCP header in 32-bit words.
The optional and variable-length options field is used when a sender and receiver negotiate the maximum segment size (MSS)

## Slide 61: TCP Segment Structure (cont..)
The flag field contains 6 bits.
The ACK bit is used to indicate that the value carried in the acknowledgment field is valid
The RST, SYN, and FIN bits are used for connection setup and teardown
PSH bit indicates that the receiver should pass the data to the upper layer immediately
The URG bit is used to indicate that there is data in this segment that the sending-side upper-layer entity has marked as “urgent.” The location of the last byte of this urgent data is indicated by the 16-bit urgent data pointer field.

## Slide 62: TCP seq. numbers, ACKs
sequence numbers:
byte stream “number” of first byte in segment’s data
acknowledgements:
seq # of next byte expected from other side
cumulative ACK
Q: how receiver handles out-of-order segments
A: TCP spec doesn’t say,
- up to implementor
source port # |  |  |  | dest port #
sequence number |  |  |  | 
acknowledgement number |  |  |  | 
 |  | A |  | rwnd
checksum |  |  |  | urg pointer
sent sent, not- ACKed
usable not
yet ACKed but not usable (“in-flight”) yet sent
incoming segment to sender
window size
N
sender sequence number space
source port #
dest port #
sequence number
acknowledgement number
checksum
rwnd
urg pointer
outgoing segment from sender

## Slide 63: TCP seq. numbers, ACKs
User types
‘C’
host ACKs
receipt of echoed
‘C’
host ACKs receipt of ‘C’, echoes back ‘C’
simple telnet scenario
Host B
Host A
Seq=42, ACK=79, data = ‘C’
Seq=79, ACK=43, data = ‘C’
Seq=43, ACK=80

## Slide 64: TCP round trip time, timeout
Q: how to set TCP timeout value?
longer than RTT
 but RTT varies
too short: premature timeout, unnecessary retransmissions
too long: slow reaction to segment loss


Q: how to estimate RTT?
SampleRTT: measured time from segment transmission until ACK receipt
ignore retransmissions
SampleRTT will vary, want estimated RTT “smoother”
average several recent measurements, not just current SampleRTT

## Slide 65: TCP round trip time, timeout
Transport Layer 3-62
RTT: gaia.cs.umass.edu to fantasia.eurecom.fr
100
150
200
250
300
350
1
8
15
22
29
71
78
85
92
99
106
time (seconnds)
SampleRTT Estimated RTT
)
s
d
n
o
c
e
s
i
l
l
i
m (
T
T R
EstimatedRTT = (1- )*EstimatedRTT + *SampleRTT



exponential weighted moving average
influence of past sample decreases exponentially fast typical value:  = 0.125
) sdnocesilli m( TTR
RTT: gaia.cs.umass.edu to fantasia.eurecom.fr
sampleRTT
EstimatedRTT
36 43 50 57 64
time (seconds)

## Slide 66: TCP round trip time, timeout
 timeout interval: EstimatedRTT plus “safety margin”
 large variation in EstimatedRTT -> larger safety margin

estimate SampleRTT deviation from EstimatedRTT:
DevRTT = (1- )*DevRTT +
 *|SampleRTT-EstimatedRTT|
(typically,  = 0.25)
TimeoutInterval = EstimatedRTT + 4*DevRTT
estimated RTT
“safety margin”

## Slide 67: Chapter 3 outline
  transport-layer services
  multiplexing and demultiplexing
  connectionless transport: UDP
  principles of reliable data transfer
  connection-oriented transport: TCP
    segment structure
    reliable data transfer
    flow control
    connection management
  principles of congestion control
  TCP congestion control

## Slide 68: TCP reliable data transfer
cumulative acks
single retransmission timer
retransmissions triggered by:
  timeout events
  duplicate acks
 TCP creates rdt service on top of IP’s unreliable service
 pipelined segments
let’s initially consider
simplified TCP sender:
ignore duplicate acks
ignore flow control, congestion control

## Slide 69: TCP sender events:
data rcvd from app:
create segment with seq #
seq # is byte-stream number of first data byte in segment
start timer if not already running
  think of timer as for oldest unacked segment
  expiration interval:
TimeOutInterval
timeout:
retransmit segment that caused timeout
restart timer
ack rcvd:
if ack acknowledges previously unacked segments
  update what is known to be ACKed
  start timer if there are still unacked segments

## Slide 70: TCP sender (simplified)
Transport Layer 3-67
wait for event
 
NextSeqNum = InitialSeqNum SendBase = InitialSeqNum
pass segment to IP (i.e., “send”) NextSeqNum = NextSeqNum + length(data) if (timer currently not running)
start timer
data received from application above create segment, seq. #: NextSeqNum
timeout
retransmit not-yet-acked segment
with smallest seq. #
start timer
ACK received, with ACK field value y
if (y > SendBase) { SendBase = y
/* SendBase–1: last cumulatively ACKed byte */ if (there are currently not-yet-acked segments)
start timer
else stop timer
}

## Slide 71: TCP: retransmission scenarios
lost ACK scenario
Host B
Seq=92, 8 bytes of data
ACK=100
Seq=92, 8 bytes of data
X
t uoe mit
ACK=100
premature timeout
Host B
Host A Host A
Seq=92, 8 bytes of data
Seq=92, 8
bytes of data
t uoe mit
ACK=120
Seq=100, 20 bytes of data
ACK=100
ACK=120
SendBase=100
SendBase=120
SendBase=120
SendBase=92

## Slide 72: TCP: retransmission scenarios
cumulative ACK
Host B
Host A
Seq=120, 15 bytes of data
Seq=92, 8 bytes of data
Seq=100, 20 bytes of data
ACK=100
X
ACK=120
t uoe mit

## Slide 73: TCP ACK generation
[RFC 1122, RFC 2581]
event at receiver
arrival of in-order segment with expected seq #. All data up to expected seq # already ACKed
arrival of in-order segment with expected seq #. One other segment has ACK pending
arrival of out-of-order segment higher-than-expect seq. # .
Gap detected
arrival of segment that partially or completely fills gap
TCP receiver action
delayed ACK. Wait up to 500ms
for next segment. If no next segment, send ACK
immediately send single cumulative ACK, ACKing both in-order segments
immediately send duplicate ACK, indicating seq. # of next expected byte
immediate send ACK, provided that segment starts at lower end of gap

## Slide 74: TCP fast retransmit
time-out period often relatively long:
  long delay before resending lost packet
detect lost segments via duplicate ACKs.
  sender often sends many segments back- to-back
  if segment is lost, there will likely be many duplicate ACKs.
(“triple duplicate ACKs”),
TCP fast retransmit
if sender receives 3 ACKs for same data
(“triple duplicate ACKs”), resend unacked segment with smallest seq #
 likely that unacked segment lost, so don’t wait for timeout

## Slide 75: TCP fast retransmit
fast retransmit after sender receipt of triple duplicate ACK
Host B
Host A
Seq=92, 8 bytes of data Seq=100, 20 bytes of data
X
ACK=100 ACK=100 ACK=100 ACK=100
Seq=100, 20 bytes of data
t uoe mit

## Slide 76: Chapter 3 outline
  transport-layer services
  multiplexing and demultiplexing
  connectionless transport: UDP
  principles of reliable data transfer
  connection-oriented transport: TCP
    segment structure
    reliable data transfer
    flow control
    connection management
  principles of congestion control
  TCP congestion control

## Slide 77: TCP flow control
application process
TCP socket receiver buffers
TCP
code
IP
code
application
OS
receiver protocol stack
application may remove data from TCP socket buffers ….
… slower than TCP receiver is delivering (sender is sending)
from sender
receiver controls sender, so sender won’t overflow receiver’s buffer by transmitting too much, too fast
flow control

## Slide 78: TCP flow control
buffered data
free buffer space
rwnd
RcvBuffer
TCP segment payloads
to application process

receiver “advertises” free buffer space by including rwnd value in TCP header of receiver-to-sender segments
RcvBuffer size set via socket options (typical default is 4096 bytes)
many operating systems autoadjust RcvBuffer
sender limits amount of unacked (“in-flight”) data to receiver’s rwnd value
guarantees receive buffer will not overflow


receiver-side buffering

## Slide 79: Chapter 3 outline
  transport-layer services
  multiplexing and demultiplexing
  connectionless transport: UDP
  principles of reliable data transfer
  connection-oriented transport: TCP
    segment structure
    reliable data transfer
    flow control
    connection management
  principles of congestion control
  TCP congestion control

## Slide 80: Connection Management
before exchanging data, sender/receiver “handshake”:

agree to establish connection (each knowing the other willing to establish connection)
agree on connection parameters

connection state: ESTAB connection variables:
seq # client-to-server server-to-client
rcvBuffer size at server,client
application
network
connection state: ESTAB connection Variables:
seq # client-to-server
server-to-client
rcvBuffer size at server,client
application
network
Socket clientSocket = newSocket("hostname","port number");
Socket connectionSocket = welcomeSocket.accept();

## Slide 81: Agreeing to establish a connection


variable delays
retransmitted messages (e.g. req_conn(x)) due to message loss
message reordering can’t “see” other side


2-way handshake:
Q: will 2-way handshake always work in network?
Let’s talk
OK
ESTAB
ESTAB
choose x
req_conn(x)
ESTAB
ESTAB
acc_conn(x)

## Slide 82: Agreeing to establish a connection
2-way handshake failure scenarios:
retransmit req_conn(x)
ESTAB
ESTAB
req_conn(x)
half open connection! (no client!)
client terminates
server forgets x
connection x completes
data(x+1)
ESTAB
accept data(x+1)
choose x
req_conn(x)
ESTAB
acc_conn(x)
client terminates
retransmit req_conn(x)
ESTAB
retransmit data(x+1)
choose x
req_conn(x)
ESTAB
acc_conn(x)
data(x+1)
accept data(x+1)
connection x completes
server
req_conn(x) forgets x

## Slide 83: TCP 3-way handshake
SYNbit=1, Seq=x
choose init seq num, x send TCP SYN msg
ESTAB
SYNbit=1, Seq=y ACKbit=1; ACKnum=x+1
choose init seq num, y send TCP SYNACK msg, acking SYN
ACKbit=1, ACKnum=y+1
received SYNACK(x) indicates server is live; send ACK for SYNACK; this segment may contain client-to-server data
received ACK(y) indicates client is live
SYNSENT
ESTAB
SYN RCVD
client state
LISTEN
server state
LISTEN

## Slide 84: TCP 3-way handshake: FSM
closed

listen
SYN
rcvd
SYN
sent
ESTAB
Socket clientSocket = newSocket("hostname","port
number");
SYN(seq=x)
Socket connectionSocket = welcomeSocket.accept();
SYN(x)
SYNACK(seq=y,ACKnum=x+1) create new socket for communication back to client
SYNACK(seq=y,ACKnum=x+1) ACK(ACKnum=y+1)
ACK(ACKnum=y+1)


## Slide 85: TCP: closing a connection
client, server each close their side of connection
  send TCP segment with FIN bit = 1
respond to received FIN with ACK
  on receiving FIN, ACK can be combined with own FIN
simultaneous FIN exchanges can be handled

## Slide 86: TCP: closing a connection
FIN_WAIT_2
CLOSE_WAIT
FINbit=1, seq=y
ACKbit=1; ACKnum=y+1
ACKbit=1; ACKnum=x+1
wait for server
close
can still send data
can no longer send data
LAST_ACK
CLOSED
TIMED_WAIT
timed wait for 2*max segment lifetime
CLOSED
FIN_WAIT_1
FINbit=1, seq=x
can no longer send but can receive data
clientSocket.close()
client state
ESTAB
server state
ESTAB

## Slide 87: Chapter 3 outline
  transport-layer services
  multiplexing and demultiplexing
  connectionless transport: UDP
  principles of reliable data transfer
  connection-oriented transport: TCP
    segment structure
    reliable data transfer
    flow control
    connection management
  principles of congestion control
  TCP congestion control

## Slide 88: Principles of congestion control
congestion:
informally: “too many sources sending too much data too fast for network to handle”
different from flow control!
manifestations:
  lost packets (buffer overflow at routers)
  long delays (queueing in router buffers)
a top-10 problem!

## Slide 89: Causes/costs of congestion: scenario 1

two senders, two receivers
one router, infinite buffers
output link capacity: R no retransmission




maximum per-connection throughput: R/2
unlimited shared output link buffers
Host A
original data: in
Host B
throughput: 
out
R/2
R/2
out
in
R/2
delay
in

large delays as arrival rate,
in, approaches capacity

## Slide 90: Causes/costs of congestion: scenario 2
one router, finite buffers
sender retransmission of timed-out packet
 application-layer input = application-layer output: in = out
 transport-layer input includes retransmissions : ‘in
in
Host A

out
in : original data
'in: original data, plus
retransmitted data
finite shared output
link buffers
Host B

## Slide 91: Causes/costs of congestion: scenario 2
idealization: perfect knowledge

sender sends only when router buffers available

out
in : original data
'in: original data, plus
retransmitted data
copy
free buffer space!
R/2
R/2
out
in
finite shared output
link buffers
Host B
A

## Slide 92: Causes/costs of congestion: scenario 2

out
in : original data
'in: original data, plus
retransmitted data
copy
no buffer space!
Idealization: known loss packets can be lost, dropped at router due to full buffers

sender only resends if packet known to be lost
Host B
A

## Slide 93: Causes/costs of congestion: scenario 2

out
in : original data
'in: original data, plus
retransmitted data
free buffer space!
Idealization: known loss packets can be lost, dropped at router due to full buffers

sender only resends if packet known to be lost
R/2
R/2

in
out
when sending at R/2, some packets are retransmissions but asymptotic goodput is still R/2 (why?)
A
Host B

## Slide 94: Causes/costs of congestion: scenario 2
A

out
in
'in
copy
free buffer space!
timeout
R/2
R/2

in
out
when sending at R/2, some packets are retransmissions including duplicated that are delivered!
Realistic: duplicates

packets can be lost, dropped at router due to full buffers
sender times out prematurely, sending two copies, both of which are delivered

Host B

## Slide 95: Causes/costs of congestion: scenario 2
R/2
out
when sending at R/2, some packets are retransmissions including duplicated that are delivered!
“costs” of congestion:


more work (retrans) for given “goodput”
unneeded retransmissions: link carries multiple copies of pkt
 decreasing goodput
R/2

in
Transport Layer 3-95
Realistic: duplicates

packets can be lost, dropped at router due to full buffers
sender times out prematurely, sending two copies, both of which are delivered


## Slide 96: Causes/costs of congestion: scenario 3



four senders multihop paths timeout/retransmit
Q: what happens as in and in’
increase ?
link buffers
Host A
Host B
Host C
Host D
 : original data out
in
'in: original data, plus
retransmitted data finite shared output
’
A: as red in increases, all arriving
blue pkts at upper queue are dropped, blue throughput  0
Transport Layer 3-96

## Slide 97: Causes/costs of congestion: scenario 3
another “cost” of congestion:
 when packet dropped, any “upstream transmission capacity used for that packet was wasted!
C/2
Transport Layer 3-97
C/2
out
in’

## Slide 98: Approaches towards congestion control
two broad approaches towards congestion control:
end-end congestion control:



no explicit feedback from network
congestion inferred from end-system observed loss, delay
approach taken by TCP
network-assisted congestion control:
Transport Layer 3-98
routers provide feedback to end systems
  single bit indicating congestion (SNA, DECbit, TCP/IP ECN, ATM)
  explicit rate for sender to send at

## Slide 99: Case study: ATM ABR congestion control
ABR: available bit rate:


“elastic service”
if sender’s path “underloaded”:
sender should use available bandwidth
if sender’s path congested:
sender throttled to minimum guaranteed rate




RM (resource management) cells:
sent by sender, interspersed with data cells
bits in RM cell set by switches (“network-assisted”)
NI bit: no increase in rate (mild congestion)
CI bit: congestion indication
RM cells returned to sender by receiver, with bits intact
Transport Layer 3-99

## Slide 100: Case study: ATM ABR congestion control
two-byte ER (explicit rate) field in RM cell
  congested switch may lower ER value in cell
  senders’ send rate thus max supportable rate on path
EFCI bit in data cells: set to 1 in congested switch
  if data cell preceding RM cell has EFCI set, receiver sets CI bit in returned RM cell
RM cell
Transport Layer 3-100
data cell

## Slide 101: Chapter 3 outline
  transport-layer services
  multiplexing and demultiplexing
  connectionless transport: UDP
  principles of reliable data transfer
  connection-oriented transport: TCP
    segment structure
    reliable data transfer
    flow control
    connection management
  principles of congestion control
  TCP congestion control
Transport Layer 3-101

## Slide 102: TCP congestion control: additive increase
multiplicative decrease
approach: sender increases transmission rate (window size), probing for usable bandwidth, until loss occurs
  additive increase: increase cwnd by 1 MSS every RTT until loss detected
  multiplicative decrease: cut cwnd in half after loss
cwnd: TCP sender congestion window size
AIMD saw tooth behavior: probing for bandwidth
additively increase window size …
…. until loss occurs (then cut window in half)
time
Transport Layer 3-102

## Slide 103: TCP Congestion Control: details
 sender limits transmission:
 cwnd is dynamic, function of perceived network congestion
TCP sending rate:
 roughly: send cwnd bytes, wait RTT for ACKS, then send more bytes
last byte ACKed
sent, not-
yet ACKed (“in-flight”)
last byte sent
cwnd
LastByteSent- LastByteAcked
<
cwnd
sender sequence number space
rate
~
cwnd bytes/sec RTT
Transport Layer 3-103

## Slide 104: TCP Slow Start
when connection begins, increase rate exponentially until first loss event:
  initially cwnd = 1 MSS
  double cwnd every RTT
  done by incrementing cwnd for every ACK received
summary: initial rate is slow but ramps up exponentially fast
Host A
one segment
RTT
Host B
time
two segments
four segments
Transport Layer 3-104

## Slide 105: TCP: detecting, reacting to loss
Transport Layer 3-105
loss indicated by timeout:
  cwnd set to 1 MSS;
  window then grows exponentially (as in slow start) to threshold, then grows linearly
loss indicated by 3 duplicate ACKs: TCP RENO
  dup ACKs indicate network capable of delivering some segments
  cwnd is cut in half window then grows linearly
TCP Tahoe always sets cwnd to 1 (timeout or 3 duplicate acks)

## Slide 106: TCP: switching from slow start to CA
Q: when should the exponential increase switch to linear?
A: when cwnd gets to 1/2 of its value before timeout.
Implementation:


variable ssthresh
on loss event, ssthresh is set to 1/2 of cwnd just before loss event
Transport Layer 3-106

## Slide 107: Summary: TCP Congestion Control
timeout ssthresh = cwnd/2
cwnd = 1 MSS dupACKcount = 0
retransmit missing segment
cwnd > ssthresh

congestion avoidance
cwnd = cwnd + MSS (MSS/cwnd) dupACKcount = 0
transmit new segment(s), as allowed
new AC
K.
dupACKcount++
duplicate ACK
fast recovery
duplicate ACK
cwnd = cwnd + MSS
transmit new segment(s), as allowed
ssthresh= cwnd/2 cwnd = ssthresh + 3
retransmit missing segment
dupACKcount == 3
timeout
ssthresh = cwnd/2
cwnd = 1
dupACKcount = 0
retransmit missing segment
ssthresh= cwnd/2 cwnd = ssthresh + 3
retransmit missing segment
dupACKcount == 3
cwnd = ssthresh dupACKcount = 0
New ACK
slow start
timeout
s
sthresh = cwnd/2 cwnd = 1 MSS dupACKcount = 0
retransmit missing segment
new ACK
cwnd = cwnd+MSS dupACKcount = 0
transmit new segment(s), as allowed
dupACKcount++
duplicate ACK

cwnd = 1 MSS ssthresh = 64 KB
dupACKcount = 0
New
ACK!
New
ACK!
New
ACK!
Transport Layer 3-107

## Slide 108: TCP throughput
avg. TCP thruput as function of window size, RTT?
  ignore slow start, assume always data to send
W: window size (measured in bytes) where loss occurs
  avg. window size (# in-flight bytes) is ¾ W
  avg. thruput is 3/4W per RTT
W
Transport Layer 3-108
W/2
avg TCP thruput = 3
W
4 RTT
bytes/sec

## Slide 109: TCP Futures: TCP over “long, fat pipes”
example: 1500 byte segments, 100ms RTT, want 10 Gbps throughput
requires W = 83,333 in-flight segments
throughput in terms of segment loss probability, L
[Mathis 1997]:
➜ to achieve 10 Gbps throughput, need a loss rate of L
= 2·10-10 – a very small loss rate!
 new versions of TCP for high-speed
TCP throughput = 1.22 . MSS
RTT
L
Transport Layer 3-109

## Slide 110: TCP Fairness
fairness goal: if K TCP sessions share same bottleneck link of bandwidth R, each should have average rate of R/K
TCP connection 1
bottleneck router capacity R
TCP connection 2
Transport Layer 3-110

## Slide 111: Why is TCP fair?
two competing sessions:


additive increase gives slope of 1, as throughout increases multiplicative decrease decreases throughput proportionally
R
R
equal bandwidth share
Connection 1 throughput
Connection 2 throughput
loss: decrease window by factor of 2 congestion avoidance: additive increase
loss: decrease window by factor of 2 congestion avoidance: additive increase
Transport Layer 3-111

## Slide 112: Fairness (more)
Transport Layer 3-112
Fairness and UDP
multimedia apps often do not use TCP
  do not want rate throttled by congestion control
instead use UDP:
  send audio/video at constant rate, tolerate packet loss
Fairness, parallel TCP connections
application can open multiple parallel connections between two hosts
web browsers do this
e.g., link of rate R with 9 existing connections:
  new app asks for 1 TCP, gets rate R/10
  new app asks for 11 TCPs, gets R/2

## Slide 113: Chapter 3: summary
Transport Layer 3-113
principles behind transport layer services:
  multiplexing, demultiplexing
  reliable data transfer
  flow control
  congestion control
instantiation, implementation in the Internet
  UDP
  TCP
next:
leaving the network “edge” (application, transport layers)
into the network “core”