## Slide 1: Chapter 4 Network Layer
Computer Networking: A Top Down Approach
6th edition
Jim Kurose, Keith Ross Addison-Wesley March 2012
A note on the use of these ppt slides:
We’re making these slides freely available to all (faculty, students, readers). They’re in PowerPoint form so you see the animations; and can add, modify, and delete slides (including this one) and slide content to suit your needs.
They obviously represent a lot of work on our part. In return for use, we only ask the following:
If you use these slides (e.g., in a class) that you mention their source
(after all, we’d like people to use our book!)
If you post any slides on a www site, that you note that they are adapted from (or perhaps identical to) our slides, and note our copyright of this material.
Thanks and enjoy! JFK/KWR
All material copyright 1996-2013
J.F Kurose and K.W. Ross, All Rights Reserved

## Slide 2: Chapter 4: network layer
chapter goals:
understand principles behind network layer services:
  network layer service models
  forwarding versus routing
  how a router works
  routing (path selection)
  broadcast, multicast
instantiation, implementation in the Internet

## Slide 3: Chapter 4: outline
  introduction
  virtual circuit and datagram networks
  what’s inside a router
  IP: Internet Protocol
    datagram format
    IPv4 addressing
    ICMP
    IPv6
  routing algorithms
    link state
    distance vector
    hierarchical routing
  routing in the Internet
    RIP
    OSPF
    BGP
  broadcast and multicast routing

## Slide 4: Network layer
 transport segment from sending to receiving host

on sending side encapsulates segments into datagrams
on receiving side, delivers segments to transport layer
network layer protocols in every host, router
router examines header fields in all IP datagrams passing through it
application
transport
network
data link
physical
application
transport
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
ne
twork
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical

## Slide 5: Two key network-layer functions
forwarding: move packets from router’s input to appropriate router output
routing: determine route taken by packets from source to dest.
 routing algorithms
analogy:
routing: process of planning trip from source to dest
forwarding: process of getting through single interchange

## Slide 6: Interplay between routing and forwarding
1
2
3
0111
value in arriving packet’s header
routing algorithm
local forwarding table
header value output link
0100 | 3
0101 | 2
0111 | 2
1001 | 1
routing algorithm determines
end-end-path through network forwarding table determines
local forwarding at this router

## Slide 7: Connection setup
3rd important function in some network architectures:
  ATM, frame relay, X.25
before datagrams flow, two end hosts and
intervening routers establish virtual connection
  routers get involved
network vs transport layer connection service:
  network: between two hosts (may also involve intervening routers in case of VCs)
  transport: between two processes

## Slide 8: Network service model
Q: What service model for “channel” transporting datagrams from sender to receiver?
example services for individual datagrams:


guaranteed delivery
guaranteed delivery with less than 40 msec delay
example services for a flow of datagrams:

in-order datagram delivery
guaranteed minimum bandwidth to flow
restrictions on changes in inter-packet spacing



## Slide 9: Network layer service models:
Network Architecture | Service Model | Bandwidth | Guarantees ? Loss Order Timing |  |  | Congestion feedback
Internet | best effort | none | no | no | no | no (inferred
 |  |  |  |  |  | via loss)
ATM | CBR | constant rate | yes | yes | yes | no congestion
ATM | VBR | guaranteed rate | yes | yes | yes | no congestion
ATM | ABR | guaranteed minimum | no | yes | no | yes
ATM | UBR | none | no | yes | no | no

## Slide 10: Chapter 4: outline
  introduction
  virtual circuit and datagram networks
  what’s inside a router
  IP: Internet Protocol
    datagram format
    IPv4 addressing
    ICMP
    IPv6
  routing algorithms
    link state
    distance vector
    hierarchical routing
  routing in the Internet
    RIP
    OSPF
    BGP
  broadcast and multicast routing

## Slide 11: Connection, connection-less service
datagram network provides network-layer
connectionless service
virtual-circuit network provides network-layer
connection service
analogous to TCP/UDP connecton-oriented / connectionless transport-layer services, but:
  service: host-to-host
  no choice: network provides one or the other
  implementation: in network core

## Slide 12: Virtual circuits


call setup, teardown for each call before data can flow
each packet carries VC identifier (not destination host address)
every router on source-dest path maintains “state” for each passing connection
link, router resources (bandwidth, buffers) may be allocated to VC (dedicated resources = predictable service)


“source-to-dest path behaves much like telephone circuit”
performance-wise
network actions along source-to-dest path

## Slide 13: VC implementation
a VC consists of:
path from source to destination
VC numbers, one number for each link along path
entries in forwarding tables in routers along path

packet belonging to VC carries VC number (rather than dest address)
VC number can be changed on each link.


new VC number comes from forwarding table

## Slide 14: VC forwarding table
12
22
32
1
2
3
VC number
interface number
Incoming VC #
Outgoing interface
Outgoing VC #
1 | 12 | 3 |  | 22 | 
2 | 63 | 1 |  | 18 | 
3 | 7 | 2 |  | 17 | 
1 | 97 | 3 |  | 87 | 
… | … |  | … |  | …
forwarding table in northwest router:
Incoming interface
VC routers maintain connection state information!

## Slide 15: Virtual circuits: signaling protocols
application
transport
network
data link
physical
used to setup, maintain teardown VC
used in ATM, frame-relay, X.25
not used in today’s Internet
2. incoming call
3. accept call
5. data flow begins
4. call connected
1. initiate call
6. receive data
application
transport
network
data link
physical

## Slide 16: Datagram networks
no call setup at network layer
routers: no state about end-to-end connections
 no network-level concept of “connection”
packets forwarded using destination host address
1. send datagrams
application
transport
network
data link
physical
application
transport
network
data link
physical
2. receive datagrams

## Slide 17: Datagram Networks (Cont..)
As a packet is transmitted from source to destination, it passes through a series of routers. Each of these routers uses the packet’s destination address to forward the packet. Specifically, each router has a forwarding table that maps destination addresses to link interfaces; when a packet arrives at the router, the router uses the packet’s destination address to look up the appropriate output link interface in the forwarding table. The router then intentionally forwards the packet to that output link interface

## Slide 18: Datagram forwarding table
IP destination address in arriving packet’s header
1
3 2
routing algorithm
local forwarding table | 
dest address | output
address-range 1 | 3 link
address-range 2 | 2
address-range 3 | 2
address-range 4 | 1
4 billion IP addresses, so rather than list individual destination address
list range of addresses
(aggregate table entries)

## Slide 19: Datagram forwarding table
Destination Address Range |  |  |  | Link Interface
11001000 through 11001000 | 00010111 00010111 | 00010000 00010111 | 00000000 11111111 | 0
11001000 through 11001000 | 00010111 00010111 | 00011000 00011000 | 00000000 11111111 | 1
11001000 through | 00010111 | 00011001 | 00000000 | 2
11001000 | 00010111 | 00011111 | 11111111 | 
otherwise |  |  |  | 3
Q: but what happens if ranges don’t divide up so nicely?

## Slide 20: Longest prefix matching
Destination Address Range |  |  |  | Link interface
11001000 | 00010111 | 00010*** | ********* | 0
11001000 | 00010111 | 00011000 | ********* | 1
11001000 | 00010111 | 00011*** | ********* | 2
otherwise |  |  |  | 3
DA: 11001000 00010111 00011000 10101010
examples:
DA: 11001000 00010111 00010110 10100001
which interface? which interface?
longest prefix matching
when looking for forwarding table entry for given destination address, use longest address prefix that matches destination address.

## Slide 21: Datagram or VC network: why?

data exchange among computers
“elastic” service, no strict timing req.
many link types
different characteristics
uniform service difficult
“smart” end systems (computers)
can adapt, perform control, error recovery
simple inside network, complexity at “edge”
Internet (datagram) ATM (VC)




evolved from telephony human conversation:
 strict timing, reliability requirements

need for guaranteed service

“dumb” end systems
telephones
complexity inside network

## Slide 22: Chapter 4: outline
  introduction
  virtual circuit and datagram networks
  what’s inside a router
  IP: Internet Protocol
    datagram format
    IPv4 addressing
    ICMP
    IPv6
  routing algorithms
    link state
    distance vector
    hierarchical routing
  routing in the Internet
    RIP
    OSPF
    BGP
  broadcast and multicast routing

## Slide 23: Router architecture overview
two key router functions:


run routing algorithms/protocol (RIP, OSPF, BGP)
forwarding datagrams from incoming to outgoing link
high-seed switching fabric
routing processor
router input ports
router output ports
forwarding data plane (hardware)
routing, management control plane (software)
forwarding tables computed,
pushed to input ports

## Slide 24: Input port functions
line termination
link layer protocol (receive)
lookup, forwarding
queueing
decentralized switching:

given datagram dest., lookup output port using forwarding table in input port memory (“match plus action”)
goal: complete input port processing at ‘line speed’
queuing: if datagrams arrive faster than forwarding rate into switch fabric


physical layer: bit-level reception
data link layer: e.g., Ethernet see chapter 5
switch fabric

## Slide 25: Switching fabrics
transfer packet from input buffer to appropriate output buffer
switching rate: rate at which packets can be transfer from inputs to outputs
  often measured as multiple of input/output line rate
  N inputs: switching rate N times line rate desirable
three types of switching fabrics
memory
memory
bus
crossbar

## Slide 26: Switching via memory
first generation routers:
traditional computers with switching under direct control of CPU
packet copied to system’s memory
speed limited by memory bandwidth (2 bus crossings per datagram)
input port (e.g., Ethernet)
memory
output port (e.g., Ethernet)
system bus

## Slide 27: Switching via a bus
datagram from input port memory
to output port memory via a shared bus
bus contention: switching speed limited by bus bandwidth
32 Gbps bus, Cisco 5600: sufficient speed for access and enterprise routers
bus

## Slide 28: Switching via interconnection network
overcome bus bandwidth limitations
banyan networks, crossbar, other
interconnection nets initially developed to connect processors in multiprocessor
advanced design: fragmenting datagram into fixed length cells, switch cells through the fabric.
Cisco 12000: switches 60 Gbps through the interconnection network
crossbar

## Slide 29: Output ports
 buffering required from fabric faster rate
when datagrams arrive than the transmission
 scheduling
datagrams
discipline chooses among queued for transmission
line termination
link layer protocol (send)
switch fabric
datagram buffer
queueing
This slide in HUGELY important!
Datagram (packets) can be lost due to congestion, lack of buffers
Priority scheduling – who gets best performance, network neutrality

## Slide 30: Output port queueing
buffering when arrival rate via switch exceeds output line speed
queueing (delay) and loss due to output port buffer overflow!
at t, packets more from input to output
one packet time later
switch fabric
switch fabric

## Slide 31: How much buffering?
RFC 3439 rule of thumb: average buffering equal to “typical” RTT (say 250 msec) times link capacity C
 e.g., C = 10 Gpbs link: 2.5 Gbit buffer
recent recommendation: with N flows, buffering equal to
RTT. C
N

## Slide 32: Input port queuing

fabric slower than input ports combined -> queueing may occur at input queues
 queueing delay and loss due to input buffer overflow!
Head-of-the-Line (HOL) blocking: queued datagram at front of queue prevents others in queue from moving forward

output port contention: only one red datagram can be
transferred.
lower red packet is blocked
switch fabric
one packet time later: green packet experiences HOL blocking
switch fabric

## Slide 33: Chapter 4: outline
  introduction
  virtual circuit and datagram networks
  what’s inside a router
  IP: Internet Protocol
    datagram format
    IPv4 addressing
    ICMP
    IPv6
  routing algorithms
    link state
    distance vector
    hierarchical routing
  routing in the Internet
    RIP
    OSPF
    BGP
  broadcast and multicast routing

## Slide 34: The Internet network layer
transport layer: TCP, UDP
routing protocols IP protocol path selection • addressing conventions RIP, OSPF, BGP • datagram format packet handling conventions forwarding table ICMP protocol error reporting router “signaling”
link layer
physical layer
host, router network layer functions:
network
layer

## Slide 35: IP datagram format (IP V 4)
length
32 bits
data (variable length, typically a TCP or UDP segment)
header
checksum
time to live
32 bit source IP address
ver head. type of
len service
16-bit identifier
flgs
fragment offset
upper layer
32 bit destination IP address
options (if any)
total datagram length (bytes)
used for fragmentation/ reassembly
IP protocol version
number header length
(bytes)
“type” of data
max number remaining hops (decremented at each router)
upper layer protocol to deliver payload to
e.g. timestamp, record route taken, specify list of routers to visit.
how much overhead?



20 bytes of TCP 20 bytes of IP
= 40 bytes + app layer overhead
Detecting bit errors in received datagram
( low delay, high Throughput of Reliability)

## Slide 36: IP fragmentation, reassembly

network links have MTU (max.transfer size) - largest possible link-level frame
different link types, different MTUs
large IP datagram divided (“fragmented”) within net
one datagram becomes several datagrams
“reassembled” only at final destination
IP header bits used to identify, order related fragments

fragmentation:
in: one large datagram
out: 3 smaller datagrams
reassembly
…
…

## Slide 37: IP fragmentation, reassembly
 | length =4000 | ID =x | fragflag =0 | offset =0 | 
ID
=x
offset
=0
fragflag
=1
length
=1500
ID
offset
=185
fragflag
=1
length
=1500 =x
 | length =1040 | ID =x | fragflag =0 | offset =370 | 
one large datagram becomes several smaller datagrams
example:


4000 byte datagram MTU = 1500 bytes
1480 bytes in data field
offset = 1480/8

## Slide 38: Chapter 4: outline
  introduction
  virtual circuit and datagram networks
  what’s inside a router
  IP: Internet Protocol
    datagram format
    IPv4 addressing
    ICMP
    IPv6
  routing algorithms
    link state
    distance vector
    hierarchical routing
  routing in the Internet
    RIP
    OSPF
    BGP
  broadcast and multicast routing

## Slide 39: IP addressing: introduction
 IP address: 32-bit identifier for host, router
interface
interface: connection between host/router and physical link
  router’s typically have multiple interfaces
  host typically has one or two interfaces (e.g., wired Ethernet, wireless 802.11)

IP addresses associated with each interface
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.1 = 11011111 00000001 00000001 00000001
223 1 1 1

## Slide 40: IP addressing: introduction
n
223.1.1.1
Q: how are interfaces actually connected?
A: we’ll learn about that i223.1.1.2 chapter 5, 6.
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
A: wired Ethernet interfaces connected by Ethernet switches
A: wireless WiFi interfaces connected by WiFi base station
For now: don’t need to worry about how one interface is connected to another (with no intervening router)

## Slide 41: Subnets
 IP address:
subnet part - high order bits
host part - low order bits
 what’s a subnet ?
device interfaces with same subnet part of IP address
can physically reach each other without intervening router
network consisting of 3 subnets
223.1.1.1
223.1.1.3
223.1.3.1
223.1.1.2
223.1.2.1
223.1.1.4 223.1.2.9
223.1.2.2
223.1.3.27
subnet
223.1.3.2

## Slide 42: Subnets
recipe
to determine the subnets, detach each interface from its host or router, creating islands of isolated networks
each isolated network is called a subnet
223.1.3.0/24
subnet mask: /24
223.1.1.0/24
223.1.1.3
223.1.3.2
223.1.3.1
subnet
223.1.3.27
223.1.2.2
 | 223.1.2.0/24
223.1.1.1 | 
223.1.1.2 | 223.1.2.1
223.1.1.4 | 223.1.2.9

## Slide 43: Subnets
how many?
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.2
223.1.2.1
223.1.2.6
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.2
223.1.7.0
223.1.7.1
223.1.8.1 223.1.8.0
223.1.9.1
223.1.9.2

## Slide 44: IP addressing: CIDR
CIDR: Classless InterDomain Routing
subnet portion of address of arbitrary length
address format: a.b.c.d/x, where x is # bits in subnet portion of address
subnet part
11001000 00010111 00010000 00000000
200.23.16.0/23
host
part

## Slide 45: IP addresses: how to get one?
Q: How does a host get IP address?
hard-coded by system admin in a file
  Windows: control-panel->network->configuration-
>tcp/ip->properties
  UNIX: /etc/rc.config
DHCP: Dynamic Host Configuration Protocol: dynamically get address from as server
  “plug-and-play”

## Slide 46: DHCP: Dynamic Host Configuration Protocol
goal: allow host to dynamically obtain its IP address from network server when it joins network
can renew its lease on address in use
allows reuse of addresses (only hold address while connected/“on”)
support for mobile users who want to join network (more shortly)
DHCP overview:
host broadcasts “DHCP discover” msg [optional]
DHCP server responds with “DHCP offer” msg [optional]
host requests IP address: “DHCP request” msg
DHCP server sends address: “DHCP ack” msg

## Slide 47: DHCP client-server scenario
223.1.1.0/24
223.1.2.0/24
223.1.3.0/24
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.9
223.1.3.2
223.1.3.1
223.1.1.2
223.1.3.27
223.1.2.2
223.1.2.1
DHCP
server
arriving DHCP client needs
address in this
network

## Slide 48: DHCP client-server scenario
DHCP server: 223.1.2.5
arriving client
DHCP discover
src : 0.0.0.0, 68
dest.: 255.255.255.255,67
yiaddr: 0.0.0.0
transaction ID: 654
DHCP offer
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddrr: 223.1.2.4
transaction ID: 654
lifetime: 3600 secs
DHCP request
src: 0.0.0.0, 68
dest:: 255.255.255.255, 67
yiaddrr: 223.1.2.4
transaction ID: 655
lifetime: 3600 secs
DHCP ACK
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddrr: 223.1.2.4
transaction ID: 655
lifetime: 3600 secs
Broadcast: is there a DHCP server out there?
Broadcast: I’m a DHCP server! Here’s an IP address you can use
Broadcast: OK. I’ll take that IP address!
Broadcast: OK. You’ve got that IP address!

## Slide 49: DHCP: more than IP addresses
DHCP can return more than just allocated IP address on subnet:
address of first-hop router for client
name and IP address of DNS sever
network mask (indicating network versus host portion of address)

## Slide 50: DHCP: example

connecting laptop needs its IP address, addr of first-hop router, addr of DNS server: use DHCP
DHCP request encapsulated in UDP, encapsulated in IP, encapsulated in 802.1 Ethernet
Ethernet frame broadcast (dest: FFFFFFFFFFFF) on LAN,
received at router running
DHCP server
Ethernet demuxed to IP demuxed, UDP demuxed to DHCP
router with DHCP server built into router



168.1.1.1
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP

## Slide 51: DHCP: example

DCP server formulates DHCP ACK containing client’s IP address, IP address of first-hop router for client, name & IP address of DNS server
encapsulation of DHCP server, frame forwarded to client, demuxing up to DHCP at client
client now knows its IP address, name and IP address of DSN server, IP address of its first-hop router

router with DHCP server built into router
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP


## Slide 52: DHCP: Wireshark output (home LAN)
Message type: Boot Reply (2) Hardware type: Ethernet Hardware address length: 6 Hops: 0
Transaction ID: 0x6b3a11b7
Seconds elapsed: 0
Bootp flags: 0x0000 (Unicast)
Client IP address: 192.168.1.101 (192.168.1.101)
Your (client) IP address: 0.0.0.0 (0.0.0.0)
Next server IP address: 192.168.1.1 (192.168.1.1)
Relay agent IP address: 0.0.0.0 (0.0.0.0)
Client MAC address: Wistron_23:68:8a (00:16:d3:23:68:8a) Server host name not given
Boot file name not given Magic cookie: (OK)
Option: (t=53,l=1) DHCP Message Type = DHCP ACK Option: (t=54,l=4) Server Identifier = 192.168.1.1 Option: (t=1,l=4) Subnet Mask = 255.255.255.0 Option: (t=3,l=4) Router = 192.168.1.1
Option: (6) Domain Name Server
Length: 12; Value: 445747E2445749F244574092; IP Address: 68.87.71.226;
IP Address: 68.87.73.242;
IP Address: 68.87.64.146
Option: (t=15,l=20) Domain Name = "hsd1.ma.comcast.net."
reply
Message type: Boot Request (1) Hardware type: Ethernet Hardware address length: 6
Hops: 0
Transaction ID: 0x6b3a11b7
Seconds elapsed: 0
Bootp flags: 0x0000 (Unicast)
Client IP address: 0.0.0.0 (0.0.0.0)
Your (client) IP address: 0.0.0.0 (0.0.0.0)
Next server IP address: 0.0.0.0 (0.0.0.0)
Relay agent IP address: 0.0.0.0 (0.0.0.0)
Client MAC address: Wistron_23:68:8a (00:16:d3:23:68:8a)
Server host name not given Boot file name not given Magic cookie: (OK)
Option: (t=53,l=1) DHCP Message Type = DHCP Request
Option: (61) Client identifier
Length: 7; Value: 010016D323688A; Hardware type: Ethernet
Client MAC address: Wistron_23:68:8a (00:16:d3:23:68:8a)
Option: (t=50,l=4) Requested IP Address = 192.168.1.101 Option: (t=12,l=5) Host Name = "nomad"
Option: (55) Parameter Request List
Length: 11; Value: 010F03062C2E2F1F21F92B
1 = Subnet Mask; 15 = Domain Name 3 = Router; 6 = Domain Name Server 44 = NetBIOS over TCP/IP Name Server
……
request

## Slide 53: IP addresses: how to get one?
Q: how does network get subnet part of IP addr?
A: gets allocated portion of its provider ISP’s address space
ISP's block | 11001000 00010111 00010000 | 00000000 | 200.23.16.0/20
Organization 0 | 11001000 00010111 00010000 | 00000000 | 200.23.16.0/23
Organization 1 | 11001000 00010111 00010010 | 00000000 | 200.23.18.0/23
Organization 2 | 11001000 00010111 00010100 | 00000000 | 200.23.20.0/23
... | ….. | …. | ….
Organization 7 | 11001000 00010111 00011110 | 00000000 | 200.23.30.0/23

## Slide 54: Hierarchical addressing: route aggregation
“Send me anything with addresses beginning 200.23.16.0/20”
200.23.18.0/23
200.23.30.0/23
Fly-By-Night-ISP
Organization 0
200.23.16.0/23
Organization 7
Internet
Organization 1
ISPs-R-Us
“Send me anything with addresses beginning 199.31.0.0/16”
200.23.20.0/23
Organization 2
.
.
.
.
hierarchical addressing allows efficient advertisement of routing information:

## Slide 55: Hierarchical addressing: more specific routes
ISPs-R-Us has a more specific route to Organization 1
“Send me anything with addresses beginning 200.23.16.0/20”
200.23.18.0/23
200.23.30.0/23
Fly-By-Night-ISP
Organization 0
200.23.16.0/23
Organization 7
Internet
Organization 1
ISPs-R-Us
“Send me anything with addresses
beginning 199.31.0.0/16 or 200.23.18.0/23”
200.23.20.0/23
Organization 2
.
.
.
.

## Slide 56: IP addressing: the last word...
Q: how does an ISP get block of addresses?
A: ICANN: Internet Corporation for Assigned Names and Numbers http://www.icann.org/
allocates addresses
manages DNS
assigns domain names, resolves disputes

## Slide 57: NAT: network address translation
10.0.0.1
10.0.0.2
10.0.0.3
138.76.29.7
local network
(e.g., home network) 10.0.0/24
10.0.0.4
rest of Internet
datagrams with source or destination in this network have 10.0.0/24 address for source, destination (as usual)
all datagrams leaving local network have same single source NAT IP address: 138.76.29.7,different source
port numbers

## Slide 58: NAT: network address translation
motivation: local network uses just one IP address as far as outside world is concerned:
range of addresses not needed from ISP: just one IP address for all devices
can change addresses of devices in local network without notifying outside world
can change ISP without changing addresses of devices in local network
devices inside local net not explicitly addressable, visible by outside world (a security plus)

## Slide 59: NAT: network address translation
implementation: NAT router must:
outgoing datagrams: replace (source IP address, port #) of every outgoing datagram to (NAT IP address, new port #)
. . . remote clients/servers will respond using (NAT IP address, new port #) as destination addr
remember (in NAT translation table) every (source IP address, port #) to (NAT IP address, new port #) translation pair
incoming datagrams: replace (NAT IP address, new port #) in dest fields of every incoming datagram with corresponding (source IP address, port #) stored in NAT table

## Slide 60: NAT: network address translation
10.0.0.1
10.0.0.2
10.0.0.3
S: 10.0.0.1, 3345
D: 128.119.40.186, 80
1
10.0.0.4
138.76.29.7
1: host 10.0.0.1
sends datagram to 128.119.40.186, 80
NAT translation table | 
WAN side addr | LAN side addr
138.76.29.7, 5001 | 10.0.0.1, 3345
…… | ……
S: 128.119.40.186, 80
D: 10.0.0.1, 3345
4
S: 138.76.29.7, 5001
D: 128.119.40.186, 80
2
2: NAT router changes datagram source addr from 10.0.0.1, 3345 to
138.76.29.7, 5001,
updates table
D: 138.76.29.7, 5001
S: 128.119.40.186, 80 3
3: reply arrives dest. address: 138.76.29.7, 5001
4: NAT router changes datagram
dest addr from
138.76.29.7, 5001 to 10.0.0.1, 3345

## Slide 61: NAT: network address translation
16-bit port-number field:
  60,000 simultaneous connections with a single LAN-side address!
NAT is controversial:
  routers should only process up to layer 3
  violates end-to-end argument
    NAT possibility must be taken into account by app designers, e.g., P2P applications
  address shortage should instead be solved by IPv6

## Slide 62: NAT traversal problem

client wants to connect to server with address 10.0.0.1
server address 10.0.0.1 local to LAN (client can’t use it as destination addr)
only one externally visible NATed address: 138.76.29.7
solution1: statically configure NAT to forward incoming connection requests at given port to server
 e.g., (123.76.29.7, port 2500)
always forwarded to 10.0.0.1 port 25000

10.0.0.1
10.0.0.4
NAT
router
138.76.29.7
client
?

## Slide 63: NAT traversal problem

solution 2: Universal Plug and Play (UPnP) Internet Gateway Device (IGD) Protocol. Allows NATed host to:
learn public IP address (138.76.29.7)
add/remove port mappings (with lease times)
i.e., automate static NAT port map configuration
10.0.0.1
NAT
router
IGD

## Slide 64: NAT traversal problem

solution 3: relaying (used in Skype)
NATed client establishes connection to relay
external client connects to relay
relay bridges packets between to connections
138.76.29.7
client
1. connection to relay initiated
by NATed host
2. connection to relay initiated
by client
3. relaying established
NAT
router
10.0.0.1

## Slide 65: Chapter 4: outline
  introduction
  virtual circuit and datagram networks
  what’s inside a router
  IP: Internet Protocol
    datagram format
    IPv4 addressing
    ICMP
    IPv6
  routing algorithms
    link state
    distance vector
    hierarchical routing
  routing in the Internet
    RIP
    OSPF
    BGP
  broadcast and multicast routing

## Slide 66: ICMP: internet control message protocol

used by hosts & routers to communicate network- level information
error reporting: unreachable host, network, port, protocol
echo request/reply (used by ping)
network-layer “above” IP:
ICMP msgs carried in IP datagrams
ICMP message: type, code plus first 8 bytes of IP datagram causing error


Type | Code | description
0 | 0 | echo reply (ping)
3 | 0 | dest. network unreachable
3 | 1 | dest host unreachable
3 | 2 | dest protocol unreachable
3 | 3 | dest port unreachable
3 | 6 | dest network unknown
3 | 7 | dest host unknown
4 | 0 | source quench (congestion
 |  | control - not used)
8 | 0 | echo request (ping)
9 | 0 | route advertisement
10 | 0 | router discovery
11 | 0 | TTL expired
12 | 0 | bad IP header

## Slide 67: Traceroute and ICMP

source sends series of UDP segments to dest
first set has TTL =1
second set has TTL=2, etc.
unlikely port number
when nth set of datagrams arrives to nth router:
router discards datagrams
and sends source ICMP messages (type 11, code 0)
ICMP messages includes name of router & IP address





when ICMP messages arrives, source records RTTs
stopping criteria:
UDP segment eventually arrives at destination host
destination returns ICMP “port unreachable” message (type 3, code 3)
source stops
3 probes
3 probes
3 probes

## Slide 68: IPv6: motivation
initial motivation: 32-bit address space soon to be completely allocated.
additional motivation:
  header format helps speed processing/forwarding
  header changes to facilitate QoS
IPv6 datagram format:
  fixed-length 40 byte header
  no fragmentation allowed

## Slide 69: IPv6 datagram format
ver | Traffic Class | flow label |  | 
payload len |  |  | next hdr | hop limit
source address (128 bits) |  |  |  | 
destination address (128 bits) |  |  |  | 
data |  |  |  | 
32 bits

## Slide 70: IPv6 datagram format (Cont..)
Ver: Protocol Version No.
Traffic Class: identify priority among datagrams in flow
flow Label: identify datagrams in same “flow.”
Payload Length: This 16-bit value is treated as an unsigned integer giving the number of bytes in the IPv6 datagram following the fixed-length, 40-byte datagram header
next header: This field identifies the protocol to which the contents (data field) of this datagram will be delivered (for example, to TCP or UDP).
Hop Limit: The contents of this field are decremented by one by each router that forwards the datagram. If the hop limit count reaches zero, the datagram is discarded
Source address and Destination Address: Identify the 128 bit source and Destination Address
Data. This is the payload portion of the IPv6 datagram.

## Slide 71: Other changes from IPv4
checksum: removed entirely to reduce processing time at each hop
options: allowed, but outside of header, indicated by “Next Header” field
ICMPv6: new version of ICMP
  additional message types, e.g. “Packet Too Big”
  multicast group management functions

## Slide 72: Transition from IPv4 to IPv6
not all routers can be upgraded simultaneously
  no “flag days”
  how will network operate with mixed IPv4 and IPv6 routers?
tunneling: IPv6 datagram carried as payload in IPv4 datagram among IPv4 routers
IPv4 header fields
IPv4 source, dest addr
IPv6 datagram IPv4 datagram
IPv4 payload
UDP/TCP payload
IPv6 source dest addr
IPv6 header fields

## Slide 73: Tunneling
physical view:
IPv4
IPv4
A
B
IPv6
IPv6
E
IPv6
IPv6
F
C
D
logical view:
IPv4 tunnel connecting IPv6 routers
E
IPv6
IPv6
F
A
B
IPv6
IPv6

## Slide 74: Tunneling
E-to-F:
IPv6
Network Layer 4-72
flow: X src: A dest: F
data
A-to-B: IPv6
Flow: X Src: A Dest: F
data
src:B dest: E
B-to-C:
IPv6 inside IPv4
flow: X src: A dest: F
data
B-to-C:
IPv6 inside IPv4
Flow: X Src: A Dest: F
data
src:B dest: E
physical view:
A
B
IPv6
E
IPv6
IPv6
F
IPv6 IPv4
C
D
logical view:
IPv4 tunnel connecting IPv6 routers
E
IPv6
IPv6
F
A
B
IPv6
IPv6
IPv4

## Slide 75: IPv6: adoption
US National Institutes of Standards estimate [2013]:
  ~3% of industry IP routers
  ~11% of US gov’t routers
Long (long!) time for deployment, use
  20 years and counting!
  think of application-level changes in last 20 years: WWW, Facebook, …
  Why?

## Slide 76: Chapter 4: outline
  introduction
  virtual circuit and datagram networks
  what’s inside a router
  IP: Internet Protocol
    datagram format
    IPv4 addressing
    ICMP
    IPv6
  routing algorithms
    link state
    distance vector
    hierarchical routing
  routing in the Internet
    RIP
    OSPF
    BGP
  broadcast and multicast routing

## Slide 77: Interplay between routing, forwarding
2
3
IP destination address in arriving packet’s header
1
routing algorithm
local forwarding table
dest address
output
link
address-range 1
address-range 2
address-range 3
address-range 4
3
2
2
1
routing algorithm determines
end-end-path through network forwarding table determines
local forwarding at this router

## Slide 78: Graph abstraction
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
graph: G = (N,E)
N = set of routers = { u, v, w, x, y, z }
E = set of links ={ (u,v), (u,x), (v,x), (v,w), (x,w), (x,y), (w,y), (w,z), (y,z) }
aside: graph abstraction is useful in other network contexts, e.g., P2P, where N is set of peers and E is set of TCP connections

## Slide 79: Graph abstraction: costs
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
c(x,x’) = cost of link (x,x’)
e.g., c(w,z) = 5
cost could always be 1, or inversely related to bandwidth, or inversely related to congestion
cost of path (x1, x2, x3,…, xp) = c(x1,x2) + c(x2,x3) + … + c(xp-1,xp)
key question: what is the least-cost path between u and z ?
routing algorithm: algorithm that finds that least cost path

## Slide 80: Routing algorithm classification
Q: global or decentralized information?
global:

all routers have complete topology, link cost info
“link state” algorithms

decentralized:

router knows physically- connected neighbors, link costs to neighbors
iterative process of computation, exchange of info with neighbors
“distance vector” algorithms




Q: static or dynamic?
static:
routes change slowly over time
dynamic:
routes change more quickly
periodic update
in response to link cost changes

## Slide 81: Chapter 4: outline
  introduction
  virtual circuit and datagram networks
  what’s inside a router
  IP: Internet Protocol
    datagram format
    IPv4 addressing
    ICMP
    IPv6
  routing algorithms
    link state
    distance vector
    hierarchical routing
  routing in the Internet
    RIP
    OSPF
    BGP
  broadcast and multicast routing

## Slide 82: A Link-State Routing Algorithm
Dijkstra’s algorithm

net topology, link costs known to all nodes
accomplished via “link state broadcast”
all nodes have same info
computes least cost paths from one node (‘source”) to all other nodes
gives forwarding table for that node
iterative: after k iterations, know least cost path to k dest.’s


notation:
c(x,y): link cost from node x to y; = ∞ if not direct neighbors
D(v): current value of cost of path from source to dest. v
p(v): predecessor node along path from source to v
N': set of nodes whose least cost path definitively known

## Slide 83: Dijsktra’s Algorithm
1 Initialization:
2 N' = {u}
for all nodes v
if v adjacent to u
then D(v) = c(u,v)
else D(v) = ∞ 7
Loop
find w not in N' such that D(w) is a minimum
add w to N'
update D(v) for all v adjacent to w and not in N' : 12 D(v) = min( D(v), D(w) + c(w,v) )
/* new cost to v is either old cost to v or known
shortest path cost to w plus cost from w to v */
until all nodes in N'

## Slide 84: Dijkstra’s algorithm: example
w
4
v
x
u 3
5
3
7
4
y
8
z
2
7
9
4
5
D(v) D(w) D(x) D(y) D(z)
Step N' |  | p(v) | p(w) | p(x) | p(y) | p(z)
0 | u | 7,u | 3,u | 5,u | ∞ | ∞
1 | uw | 6,w |  | 5,u | 11,w | ∞
2 | uwx | 6,w |  |  | 11,w | 14,x
3 | uwxv |  |  |  | 10,v | 14,x
uwxvy
12,y
notes:


construct shortest path tree by tracing predecessor nodes
ties can exist (can be broken arbitrarily)
uwxvyz

## Slide 85: Dijkstra’s algorithm: another example
Step | N' | D(v),p(v) | D(w),p(w) | D(x),p(x) | D(y),p(y) D(z),p(z) | 
0 | u | 2,u | 5,u | 1,u | ∞ ∞ | 
1 | ux | 2,u | 4,x |  | 2,x ∞ | 
2 | uxy | 2,u | 3,y |  | 4,y | 
3 | uxyv |  | 3,y |  | 4,y | 
4 | uxyvw |  |  |  | 4,y | 
5 | uxyvwz |  |  |  |  | 
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5

## Slide 86: Dijkstra’s algorithm: example (2)
u
y
x
z
resulting shortest-path tree from u:
v w
v (u,v)
(u,x)
(u,x)
w (u,x)
z (u,x)
destination
link
resulting forwarding table in u:

## Slide 87: Dijkstra’s algorithm, discussion
algorithm complexity: n nodes



each iteration: need to check all nodes, w, not in N n(n+1)/2 comparisons: O(n2)
more efficient implementations possible: O(nlogn)
oscillations possible:

e.g., support link cost equals amount of carried traffic:
A
D
C
1
1+e
B
e
0
e
1
1
0 0
initially
B
2+e
D
given these costs, find new routing…. resulting in new costs
0
0
0
1+e 1
C
A A
B
0
D
given these costs, given these costs,
find new routing…. find new routing….
resulting in new costs resulting in new costs
2+e
1+e
1
0
C
0
A
B
2+e
D
0
0
0
1+e 1
C

## Slide 88: Chapter 4: outline
  introduction
  virtual circuit and datagram networks
  what’s inside a router
  IP: Internet Protocol
    datagram format
    IPv4 addressing
    ICMP
    IPv6
  routing algorithms
    link state
    distance vector
    hierarchical routing
  routing in the Internet
    RIP
    OSPF
    BGP
  broadcast and multicast routing

## Slide 89: Distance vector algorithm
Bellman-Ford equation (dynamic programming)
let
dx(y) := cost of least-cost path from x to y
then
dx(y) = mvin {c(x,v) + dv(y) }
cost from neighbor v to destination y cost to neighbor v
min taken over all neighbors v of x

## Slide 90: Bellman-Ford example
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
clearly, dv(z) = 5, dx(z) = 3, dw(z) = 3
node achieving minimum is next
hop in shortest path, used in forwarding table
B-F equation says:
du(z) = min { c(u,v) + dv(z),
c(u,x) + dx(z),
c(u,w) + dw(z) }
= min {2 + 5,
1 + 3,
5 + 3} = 4

## Slide 91: Distance vector algorithm
Dx(y) = estimate of least cost from x to y
  x maintains distance vector Dx = [Dx(y): y є N ]
node x:
  knows cost to each neighbor v: c(x,v)
  maintains its neighbors’ distance vectors. For each neighbor v, x maintains
Dv = [Dv(y): y є N ]

## Slide 92: Distance vector algorithm
key idea:
from time-to-time, each node sends its own distance vector estimate to neighbors
when x receives new DV estimate from neighbor, it updates its own DV using B-F equation:
Dx(y) ← minv{c(x,v) + Dv(y)} for each node y ∊ N
 under minor, natural conditions, the estimate
Dx(y) converge to the actual least cost dx(y)

## Slide 93: Distance vector algorithm
iterative, asynchronous: each local iteration caused by:


local link cost change
DV update message from neighbor
distributed:

each node notifies neighbors only when its DV changes
 neighbors then notify their neighbors if necessary
each node:
wait for (change in local link cost or msg from neighbor)
recompute estimates if DV to any dest has
changed, notify neighbors

## Slide 94
x 0 2 7
y ∞ ∞ ∞
z ∞ ∞ ∞
from
cost to
from
from
cost to
x y z
∞ ∞ ∞
7 1 0
cost to
x ∞ ∞ ∞ y
z
2 0 1
∞ ∞ ∞
x ∞ ∞ ∞ y
z
x
z
1
2
7
y
node x
table x y z
x
D (y) = min{c(x,y) + D (y), c(x,z) + D (y)}
y z
= min{2+0 , 7+1} = 2
Dx(z) = min{c(x,y) + Dy(z), c(x,z) + Dz(z)}
= min{2+1 , 7+0} = 3
x 0 2 3
y 2 0 1
z 7 1 0
time
node y
table x y z
node z table
cost to
x y z
from

## Slide 95
from
cost to
x y z
from
cost to
x y z
from
cost to
x y z
x y z
from
cost to
x y z
from
cost to
x 0 2 7
y 2 0 1
z 7 1 0
x 0 2 7
y 2 0 1
z 3 1 0
x 0 2 3
y 2 0 1
z 3 1 0
x 0 2 3
y 2 0 1
z 3 1 0
x 0 2 3
y 2 0 1
z 3 1 0
x 0 2 7
y ∞ ∞ ∞
z ∞ ∞ ∞
from
cost to
from
from
cost to
x y z
∞ ∞ ∞
7 1 0
cost to
x ∞ ∞ ∞ y
z
2 0 1
∞ ∞ ∞
x ∞ ∞ ∞ y
z
x
z
1
2
7
y
node x
table x y z
x
D (y) = min{c(x,y) + D (y), c(x,z) + D (y)}
y z
= min{2+0 , 7+1} = 2
Dx(z) = min{c(x,y) + Dy(z), c(x,z) + Dz(z)}
= min{2+1 , 7+0} = 3
x 0 2 3
y 2 0 1
z 7 1 0
time
node y
table x y z
node z table
cost to
x y z
from

## Slide 96: Distance vector: link cost changes
link cost changes:


node detects local link cost change
updates routing info, recalculates distance vector
if DV changes, notify neighbors

“good news travels fast”
x
z
1
4
50
y
1
t0 : y detects link-cost change, updates its DV, informs its neighbors.
4-96
t : z receives update from y, updates its table, computes new
1
least cost to x , sends its neighbors its DV.
t2 : y receives z’s update, updates its distance table. y’s least costs do not change, so y does not send a message to z.

## Slide 97: Distance vector: link cost changes
link cost changes:


node detects local link cost change
bad news travels slow - “count to infinity” problem!
44 iterations before algorithm stabilizes: see text

z
1
50
y
60
4
x
poisoned reverse:
4-97

If Z routes through Y to get to X :
 Z tells Y its (Z’s) distance to X is infinite (so Y won’t route to X via Z)
will this completely solve count to infinity problem?


## Slide 98: Comparison of LS and DV algorithms
4-98
message complexity

LS: with n nodes, E links, O(nE) msgs sent
DV: exchange between neighbors only
 convergence time varies

speed of convergence

LS: O(n2) algorithm requires O(nE) msgs
may have oscillations
DV: convergence time varies
may be routing loops
count-to-infinity problem

robustness: what happens if router malfunctions?
LS:
node can advertise incorrect
link cost
each node computes only its
own table
DV:
DV node can advertise incorrect path cost
each node’s table used by others
  error propagate thru network

## Slide 99: Chapter 4: outline
  introduction
  virtual circuit and datagram networks
  what’s inside a router
  IP: Internet Protocol
    datagram format
    IPv4 addressing
    ICMP
    IPv6
4-99
  routing algorithms
    link state
    distance vector
    hierarchical routing
  routing in the Internet
    RIP
    OSPF
    BGP
  broadcast and multicast routing

## Slide 100: Hierarchical routing
4-100

can’t store all dest’s in routing tables!
routing table exchange would swamp links!
scale: with 600 million administrative autonomy
destinations:


internet = network of networks
each network admin may want to control routing in its own network

our routing study thus far - idealization
all routers identical
network “flat”
… not true in practice

## Slide 101: Hierarchical routing
aggregate routers into regions, “autonomous systems” (AS)
routers in same AS run same routing protocol
  “intra-AS” routing protocol
  routers in different AS can run different intra- AS routing protocol


gateway router:
at “edge” of its own AS
has link to router in another AS
4-101

## Slide 102: Interconnected ASes
3b
1d
3a
1c
2a
AS3
AS1
AS2
1a
2c
2b
1b
Intra-AS Routing algorithm
Inter-AS Routing algorithm
Forwarding
table
3c

forwarding table configured by both intra- and inter-AS routing algorithm
intra-AS sets entries for internal dests
inter-AS & intra-AS sets entries for external dests
4-102

## Slide 103: Inter-AS tasks

suppose router in AS1 receives datagram destined outside of AS1:
 router should forward packet to gateway router, but which one?
AS1 must:
learn which dests are reachable through AS2, which through AS3
propagate this reachability info to all routers in AS1
job of inter-AS routing!
AS2
3b
AS3
3c
3a
AS1
1c
1a
1d
1b
2a
2c
2b
other
networks
other
networks
4-103

## Slide 104: Example: setting forwarding table in router 1d

suppose AS1 learns (via inter-AS protocol) that subnet x
reachable via AS3 (gateway 1c), but not via AS2
inter-AS protocol propagates reachability info to all internal routers
router 1d determines from intra-AS routing info that its interface I is on the least cost path to 1c
installs forwarding table entry (x,I)

AS2
3b
AS3
3c
3a
AS1
1c
1a
1d
1b
2a
2c
2b
other
networks
other
networks
x
…
4-102

## Slide 105: Example: choosing among multiple ASes

now suppose AS1 learns from inter-AS protocol that subnet x is reachable from AS3 and from AS2.
to configure forwarding table, router 1d must determine which gateway it should forward packets towards for dest x
 this is also job of inter-AS routing protocol!

AS2
3b
AS3
3c
3a
AS1
1c
1a
1d
1b
2a
2c
2b
other
networks
other
networks
x
……
…
?
4-105

## Slide 106: Example: choosing among multiple ASes
learn from inter-AS protocol that subnet x is reachable via multiple gateways
use routing info from intra-AS
protocol to determine costs of least-cost paths to each
of the gateways
hot potato routing: choose the gateway that has the smallest least cost
determine from forwarding table the interface I that leads to least-cost gateway.
Enter (x,I) in forwarding table

now suppose AS1 learns from inter-AS protocol that subnet x is reachable from AS3 and from AS2.
to configure forwarding table, router 1d must determine towards which gateway it should forward packets for dest x
 this is also job of inter-AS routing protocol!
hot potato routing: send packet towards closest of two routers.


4-106

## Slide 107: Chapter 4: outline
  introduction
  virtual circuit and datagram networks
  what’s inside a router
  IP: Internet Protocol
    datagram format
    IPv4 addressing
    ICMP
    IPv6
4-107
  routing algorithms
    link state
    distance vector
    hierarchical routing
  routing in the Internet
    RIP
    OSPF
    BGP
  broadcast and multicast routing

## Slide 108: Intra-AS Routing
also known as interior gateway protocols (IGP)
most common intra-AS routing protocols:
  RIP: Routing Information Protocol
  OSPF: Open Shortest Path First
  IGRP: Interior Gateway Routing Protocol (Cisco proprietary)
4-108

## Slide 109: RIP ( Routing Information Protocol)


included in BSD-UNIX distribution in 1982 distance vector algorithm
distance metric: # hops (max = 15 hops), each link has cost 1
DVs exchanged with neighbors every 30 sec in response message (aka advertisement)
each advertisement: list of up to 25 destination subnets (in IP addressing sense)
D
C
B
A
u
v
w
x
y
z
u | 1
v | 2
w | 2
x | 3
y | 3
z | 2
from router A to destination subnets:
subnet hops
4-109

## Slide 110: RIP: example
destination subnet w y | next | router A B | # hops to dest 2 2
z | B |  | 7
x | -- |  | 1
…. | …. |  | ....
w
x
y
z
A
C
routing table in router D
D
B
4-110

## Slide 111: RIP: example
w
x
y
z
A
D
B
C
routing table in router D
destination subnet w | next router # hops to dest A 2 | 
y | B A | 2 5
z | B | 7
x | -- | 1
…. | …. | ....
dest next hops
w x z
- 1
- 1
C 4
….
… ...
A-to-D advertisement
4-111

## Slide 112: RIP: link failure, recovery
4-112
if no advertisement heard after 180 sec --> neighbor/link declared dead
routes via neighbor invalidated
new advertisements sent to neighbors
neighbors in turn send out new advertisements (if tables changed)
link failure info quickly (?) propagates to entire net
poison reverse used to prevent ping-pong loops (infinite distance = 16 hops)

## Slide 113: RIP table processing
physical
link
network (IP)
forwarding table
transport (UDP)
physical
link
network
(IP)
transprt (UDP)
RIP routing tables managed by application-level
process called route-d (daemon)
advertisements sent in UDP packets, periodically repeated
routed routed
forwarding table
4-113

## Slide 114: OSPF (Open Shortest Path First)
4-114
“open”: publicly available
uses link state algorithm
  LS packet dissemination
  topology map at each node
  route computation using Dijkstra’s algorithm
OSPF advertisement carries one entry per neighbor
advertisements flooded to entire AS
  carried in OSPF messages directly over IP (rather than TCP or UDP
IS-IS routing protocol: nearly identical to OSPF

## Slide 115: OSPF “advanced” features (not in RIP)
4-115
security: all OSPF messages authenticated (to prevent malicious intrusion)
multiple same-cost paths allowed (only one path in RIP)
for each link, multiple cost metrics for different TOS (e.g., satellite link cost set “low” for best effort ToS; high for real time ToS)
integrated uni- and multicast support:
 Multicast OSPF (MOSPF) uses same topology data base as OSPF
hierarchical OSPF in large domains.

## Slide 116: Hierarchical OSPF
boundary router
backbone router
area 1
area 2
area 3
backbone
area border routers
internal routers
4-116

## Slide 117: Hierarchical OSPF
two-level hierarchy: local area, backbone.
  link-state advertisements only in area
  each nodes has detailed area topology; only know direction (shortest path) to nets in other areas.
area border routers: “summarize” distances to nets in own area, advertise to other Area Border routers.
backbone routers: run OSPF routing limited to backbone.
boundary routers: connect to other AS’s.
4-117

## Slide 118: Internet inter-AS routing: BGP
4-118

BGP (Border Gateway Protocol): the de facto inter-domain routing protocol
“glue that holds the Internet together”
BGP provides each AS a means to:
eBGP: obtain subnet reachability information from neighboring ASs.
iBGP: propagate reachability information to all AS- internal routers.
determine “good” routes to other networks based on reachability information and policy.
allows subnet to advertise its existence to rest of Internet: “I am here”



## Slide 119: BGP basics

when AS3 advertises a prefix to AS1:
AS3 promises it will forward datagrams towards that prefix
AS3 can aggregate prefixes in its advertisement
AS3
AS2
3b
3c
3a
AS1
1c
1a
1d
1b
2a
2c
2b
other
networks
other
networks

BGP session: two BGP routers (“peers”) exchange BGP messages:
advertising paths to different destination network prefixes (“path vector” protocol)
exchanged over semi-permanent TCP connections
BGP
message
4-119

## Slide 120: BGP basics: distributing path information
AS3
AS2
3b
3a
AS1
1c
1a
1d
1b
2a
2c
2b
other
networks
other
networks

4-120
using eBGP session between 3a and 1c, AS3 sends prefix reachability info to AS1.
1c can then use iBGP do distribute new prefix info to all routers in AS1
1b can then re-advertise new reachability info to AS2 over 1b-to- 2a eBGP session
when router learns of new prefix, it creates entry for prefix in its forwarding table.

eBGP session
iBGP session

## Slide 121: Path attributes and BGP routes
advertised prefix includes BGP attributes
  prefix + attributes = “route”
two important attributes:
  AS-PATH: contains ASs through which prefix advertisement has passed: e.g., AS 67, AS 17
  NEXT-HOP: indicates specific internal-AS router to next- hop AS. (may be multiple links from current AS to next- hop-AS)
gateway router receiving route advertisement uses import policy to accept/decline
  e.g., never route through AS x
  policy-based routing
4-121

## Slide 122: BGP route selection
router may learn about more than 1 route to destination AS, selects route based on:
  local preference value attribute: policy decision
  shortest AS-PATH
  closest NEXT-HOP router: hot potato routing
  additional criteria
4-122

## Slide 123: BGP messages

BGP messages exchanged between peers over TCP connection
BGP messages:
OPEN: opens TCP connection to peer and authenticates sender
UPDATE: advertises new path (or withdraws old)
KEEPALIVE: keeps connection alive in absence of UPDATES; also ACKs OPEN request
NOTIFICATION: reports errors in previous msg; also used to close connection

4-123

## Slide 124: Putting it Altogether: How Does an Entry Get Into a Router’s Forwarding Table?
Answer is complicated!
Ties together hierarchical routing (Section 4.5.3) with BGP (4.6.3) and OSPF (4.6.2).
Provides nice overview of BGP!

## Slide 125: How does entry get in forwarding table?
1
2
3
Dest IP
routing algorithms
local forwarding table
prefix
output port
138.16.64/22 3
124.12/16 2
212/8 4
………….. …
entry
Assume prefix is in another AS.

## Slide 126: How does entry get in forwarding table?
High-level overview
Router becomes aware of prefix
Router determines output port for prefix
Router enters prefix-port in forwarding table

## Slide 127: Router becomes aware of prefix
AS3
AS2
3b
3c
3a
AS1
1c
1a
1d
1b
2a
2c
2b
other
networks
other
networks
BGP
message


BGP message contains “routes”
“route” is a prefix and attributes: AS-PATH, NEXT-HOP,
…
Example: route:


Prefix:138.16.64/22 ; AS-PATH: AS3 AS131 ; NEXT-HOP: 201.44.13.125

## Slide 128: Router may receive multiple routes
AS3
AS2
3b
3c
3a
AS1
1c
1a
1d
1b
2a
2c
2b
other
networks
other
networks
BGP
message
Router may receive multiple routes for same prefix
Has to select one route

## Slide 129: Select best BGP route to prefix
 Router selects route based on shortest AS-PATH
 Example:
 AS2 AS17 to 138.16.64/22
 AS3 AS131 AS201 to 138.16.64/22
 What if there is a tie? We’ll come back to that!
select

## Slide 130: Find best intra-route to BGP route
AS3
AS2
3b
Use selected route’s NEXT-HOP attribute
 Route’s NEXT-HOP attribute is the IP address of the router interface that begins the AS PATH.
Example:
 AS-PATH: AS2 AS17 ; NEXT-HOP: 111.99.86.55
Router uses OSPF to find shortest path from 1c to 111.99.86.55
3c
3a
AS1
1c
1a
1d
1b
2a
2c
2b
other
networks
other
networks
111.99.86.55

## Slide 131: Router identifies port for route
Identifies port along the OSPF shortest path
Adds prefix-port entry to its forwarding table:
 (138.16.64/22 , port 4)
AS2
3b
AS3
3c
3a
AS1
1a
1d
1b
2a
2c
2b
other
networks
other
networks
router port
1
2 1c
3
4

## Slide 132: Hot Potato Routing
Suppose there two or more best inter-routes.
Then choose route with closest NEXT-HOP
  Use OSPF to determine which gateway is closest
  Q: From 1c, chose AS3 AS131 or AS2 AS17?

A: route AS3 AS201 since it is closer
AS2
3b
AS3
3c
3a
AS1
1c
1a
1d
1b
2a
2c
2b
other
networks
other
networks

## Slide 133: How does entry get in forwarding table?
Summary
1. Router becomes aware of prefix

via BGP route advertisements from other routers
1. Determine router output port for prefix



Use BGP route selection to find best inter-AS route
Use OSPF to find best intra-AS route leading to best inter-AS route
Router identifies router port for that best route
1. Enter prefix-port entry in forwarding table

## Slide 134: BGP routing policy



A,B,C are provider networks
X,W,Y are customer (of provider networks) X is dual-homed: attached to two networks
X does not want to route from B via X to C
.. so X will not advertise to B a route to C
A
B
C
W
X
Y
legend:
customer network:
provider network
4-134

## Slide 135: BGP routing policy (2)



A
B
C
W
X
Y
A advertises path AW to B B advertises path BAW to X
Should B advertise path BAW to C?
No way! B gets no “revenue” for routing CBAW since neither W nor C are B’s customers
B wants to force C to route to w via A
B wants to route only to/from its customers!
legend:
customer network:
provider network
4-135

## Slide 136: Why different Intra-, Inter-AS routing ?
policy:
inter-AS: admin wants control over how its traffic routed, who routes through its net.
intra-AS: single admin, so no policy decisions needed
scale:
hierarchical routing saves table size, reduced update traffic
performance:
intra-AS: can focus on performance
inter-AS: policy may dominate over performance
4-136

## Slide 137: Chapter 4: outline
  introduction
  virtual circuit and datagram networks
  what’s inside a router
  IP: Internet Protocol
    datagram format
    IPv4 addressing
    ICMP
    IPv6
4-137
  routing algorithms
    link state
    distance vector
    hierarchical routing
  routing in the Internet
    RIP
    OSPF
    BGP
  broadcast and multicast routing

## Slide 138: Broadcast routing
R1
R2
R3 R4
source duplication
R1
R2
R3
R4
in-network duplication
duplicate creation/transmission
duplicate
duplicate
4-138
deliver packets from source to all other nodes
source duplication is inefficient:
 source duplication: how does source determine recipient addresses?

## Slide 139: In-network duplication
flooding: when node receives broadcast packet, sends copy to all neighbors
  problems: cycles & broadcast storm
controlled flooding: node only broadcasts pkt if it hasn’t broadcast same packet before
  node keeps track of packet ids already broadacsted
  or reverse path forwarding (RPF): only forward packet if it arrived on shortest path between node and source
spanning tree:
  no redundant packets received by any node
4-139

## Slide 140: Spanning tree
A
B
G
D
E
c
F
A
B
G
D
E
c
F
(a) broadcast initiated at A
(b) broadcast initiated at D
first construct a spanning tree
nodes then forward/make copies only along spanning tree
4-140

## Slide 141: Spanning tree: creation
A
B
G
D
E
c
F
1
2
3
4
5
(a) stepwise construction of spanning tree (center: E)
A
B
G
D
E
c
F
(b) constructed spanning tree
center node
each node sends unicast join message to center node
 message forwarded until it arrives at a node already belonging to spanning tree
4-141

## Slide 142: Multicast routing: problem statement
goal: find a tree (or trees) connecting routers having
local mcast group members
tree: not all paths between routers used
shared-tree: same tree used by all group members
source-based: different tree from each sender to rcvrs



shared tree
source-based trees
group member
not group member
router with a group member
router without group member
legend
4-142

## Slide 143: Approaches for building mcast trees
4-143
approaches:
source-based tree: one tree per source
  shortest path trees
  reverse path forwarding
group-shared tree: group uses one tree
  minimal spanning (Steiner)
  center-based trees
…we first look at basic approaches, then specific protocols adopting these approaches

## Slide 144: Shortest path tree
 mcast forwarding tree: tree of shortest path routes from source to all receivers
 Dijkstra’s algorithm
i
router with attached group member
router with no attached group member
link used for forwarding, i indicates order link added by algorithm
LEGEND
R1
R3
R4
R5
R6
2
1
6
R7
R2 3
4
5
s: source
4-144

## Slide 145: Reverse path forwarding
4-145
if (mcast datagram received on incoming link on shortest path back to center)
then flood datagram onto all outgoing links
else ignore datagram
rely on router’s knowledge of unicast shortest path from it to sender
each router has simple forwarding behavior:

## Slide 146: Reverse path forwarding: example
 result is a source-specific reverse SPT
 may be a bad choice with asymmetric links
router with attached group member
router with no attached group member
datagram will be forwarded
LEGEND
R1
R2
R3
R4
R5
R6
R7
s: source
datagram will not be forwarded
4-146

## Slide 147: Reverse path forwarding: pruning

router with attached group member
router with no attached group member
prune message links with multicast forwarding
LEGEND
P
R1
R2
R3
R4
R5
R6
forwarding tree contains subtrees with no mcast group members
no need to forward datagrams down subtree
“prune” msgs sent upstream by router with no downstream group members
s: source
R7
P
P
4-147

## Slide 148: Shared-tree: steiner tree
steiner tree: minimum cost tree connecting all routers with attached group members
problem is NP-complete
excellent heuristics exists
not used in practice:
  computational complexity
  information about entire network needed
  monolithic: rerun whenever a router needs to join/leave
4-148

## Slide 149: Center-based trees
single delivery tree shared by all
one router identified as “center” of tree
to join:
  edge router sends unicast join-msg addressed to center router
  join-msg “processed” by intermediate routers and forwarded towards center
  join-msg either hits existing tree branch for this center, or arrives at center
  path taken by join-msg becomes new branch of tree for this router
4-149

## Slide 150: Center-based trees: example
suppose R6 chosen as center:
router with attached group member
router with no attached group member
path order in which join messages generated
LEGEND
2
1
3
1
R1
R2
R3
R4
R5
R6
R7
4-150

## Slide 151: Internet Multicasting Routing: DVMRP
4-151
DVMRP: distance vector multicast routing protocol, RFC1075
flood and prune: reverse path forwarding, source- based tree
  RPF tree based on DVMRP’s own routing tables constructed by communicating DVMRP routers
  no assumptions about underlying unicast
  initial datagram to mcast group flooded everywhere via RPF
  routers not wanting group: send upstream prune msgs

## Slide 152: DVMRP: continued…
soft state: DVMRP router periodically (1 min.) “forgets” branches are pruned:
  mcast data again flows down unpruned branch
  downstream router: reprune or else continue to receive data
routers can quickly regraft to tree
  following IGMP join at leaf
odds and ends
  commonly implemented in commercial router
4-152

## Slide 153: Tunneling
Q: how to connect “islands” of multicast routers in a “sea” of unicast routers?
physical topology logical topology
mcast datagram encapsulated inside “normal” (non- multicast-addressed) datagram
normal IP datagram sent thru “tunnel” via regular IP unicast to receiving mcast router (recall IPv6 inside IPv4 tunneling)
receiving mcast router unencapsulates to get mcast datagram
4-153

## Slide 154: PIM: Protocol Independent Multicast
not dependent on any specific underlying unicast routing algorithm (works with all)
two different multicast distribution scenarios :
dense:
group members densely packed, in “close” proximity.
bandwidth more plentiful
sparse:
# networks with group members small wrt # interconnected networks
group members “widely dispersed”
bandwidth not plentiful
4-154

## Slide 155: Consequences of sparse-dense dichotomy:
4-155

group membership by routers assumed until routers explicitly prune data-driven construction on mcast tree (e.g., RPF) bandwidth and non-group- router processing profligate
dense sparse:



no membership until routers explicitly join
receiver- driven construction of mcast tree (e.g., center- based)
bandwidth and non-group- router processing conservative



## Slide 156: PIM- dense mode
flood-and-prune RPF: similar to DVMRP but…
underlying unicast protocol provides RPF info for incoming datagram
less complicated (less efficient) downstream flood than DVMRP reduces reliance on underlying routing algorithm
has protocol mechanism for router to detect it is a leaf-node router
4-156

## Slide 157: PIM - sparse mode


center-based approach
router sends join msg to rendezvous point (RP)
intermediate routers update state and forward join
after joining via RP, router can switch to source- specific tree
increased performance: less concentration, shorter paths

join
join
join
R1
R2
R3
R4
R5
R6
all data multicast from rendezvous point
R7
rendezvous
point
4-157

## Slide 158: PIM - sparse mode
sender(s):
unicast data to RP, which distributes down RP-rooted tree
RP can extend mcast tree upstream to
source
 RP can send stop msg if no attached receivers
 “no one is listening!”
join
join
join
R1
R2
R3
R4
R5
R6
all data multicast from rendezvous point
R7
rendezvous
point
4-158

## Slide 159: Chapter 4: done!
  introduction
  virtual circuit and datagram networks
  what’s inside a router
  IP: Internet Protocol
 datagram format, IPv4 addressing, ICMP, IPv6
  routing algorithms
    link state, distance vector, hierarchical routing
  routing in the Internet
    RIP, OSPF, BGP
  broadcast and multicast routing

4-159
understand principles behind network layer services:
 network layer service models, forwarding versus routing how a router works, routing (path selection), broadcast, multicast
instantiation, implementation in the Internet
